## Slide 1: Mission Operations: ESPC Enterprise Product Generation/Distribution
Chris Sisko
NESDIS/OSPO - Mission Operations Division
Telephone: 301-817-4783
Email: Chris.A.Sisko@noaa.gov

## Slide 2: Presentation Outline
Satellite Operations Overview
ESPC – Environmental Satellite Processing Center
What is the Product Distribution and Access System?
Future NESDIS Data Operations
  Data Operations: System interface to near real-time users
  Nominal Operations
  Non-nominal Operations (COOP/Back-up)
  Top Challenges
Latest schedule information
Summary
Questions and Answers

## Slide 3: Office of Satellite and Product Operations (OSPO)
OSPO manages and directs:
satellite operations, including health and safety of the spacecraft.
central ground facilities which ingest, process, and distribute environmental satellite data and derived products to domestic and foreign users.

## Slide 4: OSPO Operational Facilities
Fairbanks, AK
Wallops, VA
College Park, MD
Suitland, MD
Fairmont, WV*
* GOES-R and JPSS (New) Backup Facility
Over 500 staff supporting or operating the satellites, receptors, and processing systems

## Slide 5: Three Observation Vantage Points
540 Miles
Polar-orbiting / LEO Operational Environmental Satellites
Geostationary Operational Environmental Satellites
Each satellite covers the Earth
twice per day
  Pole-to-pole orbit is 101 minutes and views each location at the same time of day; capability for ½ orbit dumps with JPSS-1
  Global coverage every 12 hours with one satellite
  EUMETSAT - mid-morning orbit
  NOAA - early afternoon orbit
Continuous monitoring
of the Americas
  Coverage over the same geographic location
  Constant monitoring for nowcast purposes and for forecast applications (NWP, etc.)
Deep Space
at Lagrange 1 Point
Continuous monitoring
of the Sun
  Uninterrupted view of the sun
  Information is used for solar winds monitoring for Space Weather warnings
22,300 Miles

## Slide 6: Nominal Satellite Data Flow

## Slide 7: Product Distribution and Access (PDA) Overview
NESDIS’s future enterprise distribution interface for real-time users.
A scalable Service Orientated Architecture (SOA) that functions as both a high availability and high performance distribution system.
Enables users to tailor products to meet unique mission requirements, including latency.
Enhances IT security posture by utilizing in-depth defenses against evolving threats.
PDA at NSOF (Suitland, MD) will support many missions; however, PDA at CBU (Fairmont, WV backup site) will only support the JPSS missions.
Peak Throughput:
From Externals to PDA: ~10 Gbps
From PDA to Externals: ~55 Gbps
Network to Edge: scalable up to 120 Gbps
Data Volumes:
1 GOES-R Satellite – produces ~1 TB/day
1 JPSS Satellite – produces ~4 TB/day (uncompressed)
1 JPSS Satellite – produces ~1.5 TB/day (compressed)
Note – other new satellite missions are likewise driving up the data volume sizes

## Slide 8: PDA Interface Types
Two types of PDA interfaces:
  Standard PDA interface w/ User Portal to manage subscriptions
    Push & Pull services
    Standing subscriptions
    Ad-hoc request (i.e. one-time request)
  Web Services PDA Interface to feed AWIPS Data Delivery (for NWS only)
    Pull service only
    Ad-hoc request
Data Transfer Protocols
  FTP-S - authorization credentials are encrypted, but data payload is not.
  SFTP - whole session encryption
  HTTPS Pull capability

## Slide 9: Nominal Operations
PDA supports near real-time users – prioritized according to most critical mission need.
Network infrastructure provided by NWAVE; high performance, scalable network.
PDA operators can perform load shedding of the lowest priority users – guarantees resources for highest priority users.
ESPC Help Desk provides 1st Tier of support – ESPCOperations@noaa.gov
  Phone: 301-817-3880
Operational Tier / Prioritization |  | 
Tier 1 | 1 | Life & Property / National Interest Missions
 | 2 | Int'l Agreement Missions / NRT NOAA-NASA Environmental Missions/ Launch Support-Cal Val
Tier 2 | 3 | External Mission Support (i.e. AR) / Data Preservation/Archive
 | 4 | Ops Test Support
Tier 3 | 5 | Mission (Dev) Test Support / Long Term Approved RT Request
 | 6 | Prototype / Temporary Approved Dataflows or Tests / R2O

## Slide 11: Notifications: Administrative / Outage Messages
Direct notification process (ESPC Notification Message)
  Utilizes email to contact a subscribed list of users
  Send email to ESPCoperations@noaa.gov and ask to be added to the notification list
Notification using bulletin services:
  Outages, anomalies or COOP/back-up activation:
    WMO header: NOUS71 KNES (AWIPS PIL: ADANES) for urgent notices - http://www.weather.gov/view/validProds.php?prod=ADM&node=KNES
  Routine notices such as eclipse schedules, RSOs, maneuvers, etc.:
    WMO header: NOUS72 KNES (AWIPS PIL: ADMNES) for routine notices - http://www.weather.gov/view/validProds.php?prod=ADA&node=KNES

## Slide 12: Anomaly Notification / ESPC Messages
Msg Type | Msg Title
Administrative | Suomi-NPP Drag Makeup Maneuver (DMU)
 | Suomi-NPP VIIRS Lunar Calibration with spacecraft roll (VLR)
 | Suomi-NPP Risk Mitigation Maneuver (RMM)
 | Suomi-NPP Inclination Maneuver (IM)
 | Suomi-NPP Instrument Calibration
 | Suomi-NPP Instrument Operating Mode Change
 | Suomi-NPP General Notice (Unique Situations)
Outage/Anomaly | Suomi-NPP Instrument Unknown Mode or Anomaly
 | Suomi-NPP System Data Delay
 | Suomi-NPP Ground System Anomaly
 | Suomi-NPP Satellite Anomaly
Example of various message types.

## Slide 13
Everyone, we have a problem!
Remain Calm! We are moving to the Backup/COOP site!
Suitland, MD

## Slide 14: Non-Nominal Operations – Backup/COOP
Operations transfers to Fairmont, WV (CBU)
  GOES-R transfers within minutes
  Polar mission (JPSS) within 8-12 hours
Data availability from CBU PDA:
  JPSS Mission: Prime Mission Sensor products
  GOES-R Mission: None (CMI KPPs via GRB and AWIPS/SBN only)
Fairmont, WV*
Key Performance Parameters (KPPs) - key system capabilities that must be met in order for a system to meet its operational goals.

## Slide 16: High Level Timeline / Schedule

## Slide 17: Big Data Network Communication Challenges
Chart: Time (minutes)
| 1 | 2 | 4 | 10 | 20 | 30 | 40 | 50 | 60
100 GB | 13.3333 | 6.6667 | 3.3333 | 1.3333 | 0.66667 | 0.44444 | 0.33333 | 0.26667 | 0.22222
50 GB | 6.6667 | 3.3333 | 1.6667 | 0.66667 | 0.33333 | 0.22222 | 0.16667 | 0.13333 | 0.11111
20 GB | 2.6667 | 1.3333 | 0.66667 | 0.26667 | 0.13333 | 0.088889 | 0.066667 | 0.053333 | 0.044444
Bandwidth vs. time to transfer
GB - Gigabyte
Gbps – Gigabit per second (1 Gigabit = 109 bits)
Example: If you want to receive 20 GB of data in less than 5 minutes, a bandwidth speed of at least 500 Mbps of end to end network capacity is needed
NOTE: The slowest speed in the network path determines the overall data transfer speed.

## Slide 18
PDA User Data Volume Allocation
Data Volume (per day) | FTP-S | SFTP | Bandwidth Projection* (aggregated 24 hrs) | PoP Req’d | Concurrent Sessions | Comments
50 GB/day | O | O | ~5 Mbps | No | 3 | This is the default data volume for users who are unable to determine their available bandwidth
100 GB/day | O | O | ~10 Mbps | No | 3 | Option for users with larger data needs who have sufficient network/system resources
150 GB/day |  |  | ~15 Mbps |  |  | 
250 GB/day | D | A | ~25 Mbps | A | 3 | Special authorization required from data access management group
500 GB/day |  |  | ~50 Mbps |  | 3 | 
1.0 TB/day |  |  | ~95 Mbps |  | A | 
1.5 TB/day | D | N | ~140 Mbps | Yes | A | Special authorization required from data access management group, accompanied with a technical assessment
2.0 TB/day |  |  | ~190 Mbps |  |  | 
3.0 TB/day |  |  | ~280 Mbps |  |  | 
O – Optional
D – Default
A – Authorization required
N – Not Authorized
PoP – Point of presence/dedicated route
*note – absolute bandwidth minimum, does not factor in meeting user’s latency needs based on slowest link within the network path.
Default allocation based on less stringent requirements
Basic Premium allocation based on user capabilities
Premium allocation based on critical need by user
Special allocation for select vital users with a major mission justification

## Slide 19: Summary
Evolution of PDA and significant network upgrades (ESPC 2.0) are crucial in the future mission success; those activities are on track with 1st ORR scheduled in late July (GOES-R) and later in the summer for SNPP.
The enterprise distribution system (PDA) and the associated network structure is highly scalable to meet near future data demands.
Movement of large data between from systems to users is a significant challenge – slowest link in the network path dictates the overall speed across the entire path.
New satellite mission data (NOAA and non-NOAA) are two orders of magnitude larger than our previous missions; therefore, users are dealing with Terabytes of data per day output from each spacecraft.

## Slide 20: Many Thanks!
Major Contributions from:
Katie Feiner, Donna McNamara, Paul Haggerty, Jing Han, Matt Seybold, Cherie Mumford and ESPDS Development Team

## Slide 21: Acronyms
CBU – Consolidated Backup
COOP - Continuity of Operations Plan
ESPC - Environmental Satellite Processing Center
EUMETSAT - European Organisation for the Exploitation of Meteorological Satellites
GB - Gigabyte
Gbps - Gigabit per second (1 Gigabit = 109 bits)
NESDIS - National Environmental Satellite, Data, and Information Service
NSOF - NOAA Satellite Operations Facility
OSPO - Office of Satellite and Product Operations
PDA - Product Distribution and Access
SOA - Service Orientated Architecture
TB - Terabyte (1 TB = 1012 bytes Gbps)

## Slide 22: Background Slides

## Slide 23
Future Architecture/Future Geo Operations

## Slide 24
Future Architecture/Future Polar Operations

## Slide 25: Key Performance Parameters
 | Polar Orbiting |  |  | Geostationary |  |  |  |  |  | 
Mission | SNPP/JPSS-1† | METOP-A/B/C | NOAA-19 | GOES-R† | GOES-NOP |  |  | H-8 | MET-7/9/10/(11) | 
Service / Location | Primary PM (S-NPP) | Primary AM (METOP-B) | Prime Services SARSAT, A-DCS | TBD | G13-E (75W) | G15-W (135W) | G14 (spare) | 140E | MET7 (57E) | MET9/10 (9.5E, 0)
Imagery | VIIRS* >70° N, NCC, 1.6 µm | AVHRR* > 70° N | AVHRR* > 70° N | ABI (CMI) | Imager (CMI) |  |  | AHI (CMI) | MVIRI (CMI) | SEVIRI (CMI)
Sounder IR | CrIS (TDRs) | IASI/HIRS (L1B) | HIRS (L1B) | X | X |  |  | X | X | X
Sounder microwave | ATMS (TDRs) | MHS AMSU-A/B (L1B) | MHS AMSU-A/B (L1B) | X | X |  |  | X | X | X
Re-broadcast | X | X | X | GRB | GVAR |  |  | X | X | X
Other KPPs | X | ASCAT (OSWVs) | X | X | X |  |  | X | X | X
Acronym | Description
VIIRS | Visible Infrared Imaging Radiometer Suite
CrIS | Cross-track Infrared Sounder
ATMS | Advanced Technology Microwave Sounder
IASI | Infrared Atmospheric Sounding Interferometer
HIRS | High resolution Infrared Radiation Sounder
AMSU | Advanced Microwave Sounding Unit
AHI | Advanced Himawari Imager
CMI | Cloud Moisture Imagery
KPP | Key Performance Parameter
SNPP | Suomi National Polar-orbiting Partnership
JPSS | Joint Polar Satellite System
IR | Infrared
NCC | Near Constant Constrast
Acronym | Description
ASCAT | Advanced Scatterometer
AVHRR | Advanced Very High Resolution Radiometer
ABI | Advanced Baseline Imager
GRB | GOES Rebroadcast
GVAR | GOES VARiable
MVIRI | Meteosat Visible Infra-Red Imager
SEVIRI | Spinning Enhanced Visible and Infrared Imager
OSWV | Ocean Service Wind Vector(s)
H-8 | Himawari 8
GOES | Geostationary Operational Environmental Satellite
METOP | Meteorological Operational Satellite
MET | Meteosat Geostationary Satellite
S(T)DR | Sensor (Temperature) Data Record
† Well defined KPPs
* Alaska Region
Red: Recent Changes
Note – KPPs are official for GOES-R and JPSS missions only; this list contains other missions with equivalent KPPs if so defined in the near future.