## Slide 2: Agenda
L1b vs L2+ products
Data access
Data distribution before and after Handover
GOES Rebroadcast (GRB) and Product Distribution and Access (PDA) in depth
Contingency ground segment operations

## Slide 3: What Is Handover?
Operations and Products Handover occurs 6 months after GOES-R launch
Before Handover, the GOES-R program maintains control of the satellite. After Handover, OSPO takes control of the satellite.

## Slide 4: Baseline Products
http://www.goes-r.gov/products/baseline.html
Level 1b
Level 2+
Notes: Everything highlighted in blue is a Level 1b product. Everything highlighted in green is a Level 2 product.
Cloud and Moisture Imagery (CMI) is generated from Radiances. When it’s sent to the NWS WFOs/RFCs it is sectorized and referred to as SCMI.

## Slide 5: Steps to L1b
L1b Image
L1β Data
Navigate
L1α Data
L1a Data
L0 Data
01010100110111100010101010100011010…
Calibrate
Decompress
Resample
Image credit: Dave Pogorzala
Notes: This mainly applies to ABI. Graphic rendering of the processing from raw data to an L1b image.

## Slide 6: GOES-R Data Access
Acronym | System Name | Description
GRB | GOES Rebroadcast | One channel of the space data relay service of GOES-R for Level 1b data products (ABI L1b, Space Weather L1b, and GLM L2). These data are available to all users with GRB receivers in view of a GOES-R series satellite at the East or West operational longitudes.
AWIPS | Advanced Weather Interactive Processing System | Interactive computer system that integrates meteorological and hydrological data, enabling forecasters to prepare forecasts and issue warnings. GOES-R will provide selected products through AWIPS. Sectorized Cloud and Moisture Imagery will be delivered via NOAAPORT/SBN (Satellite Broadcast Network).
HRIT/ EMWIN | High Rate Information Transmission/ Emergency Managers Weather Information Network | EMWIN is a direct service that provides users with weather forecasts, warnings, graphics and other information directly from the NWS in near real-time. The HRIT service is a new high data rate (400 Kpbs) version of today’s LRIT (Low Rate Information Transmission), broadcasting GOES-R satellite imagery and selected products to remotely-located user terminals.
PDA | Product Distribution and Access | The Environmental Satellite Processing and Distribution System (ESPDS) is responsible for receiving and storing real-time environmental satellite data and products and making them available to authorized users (ABI L1b and L2+, Space Weather L1b, and GLM L2). PDA will provide real-time distribution and access services for GOES-R users.
CLASS | Comprehensive Large Array-data Stewardship System | Web-based data archive and distribution system for NOAA’s environmental data. CLASS will provide retrospective data access and distribution services of GOES-R data to all users.

## Slide 7: Data Distribution Before Handover
Once each instrument reaches Beta Maturity, data from that instrument will populate the GRB stream and thus all downstream users including PDA
NWS determines when to release data to WFOs

## Slide 8: How will you get data before and after Handover?
1. Raw data packets downlinked to WCDAS
At WCDAS, geometric and radiometric data added to L0 which processes L0 to L1b. Also, SCMI created and GLM L2.
2a. ABI L1b, Space Wx L1b, and GLM L2 uplinked to GOES-R via GRB.
AWIPS Network Control Facility (NCF) in Silver Spring, MD
WCDAS in Wallops, VA
2b. SCMI (L2) sent to NCF through terrestrial line.
5. SCMI (L2) and some L2+ products sent to Master Ground Station via terrestrial line.
Master Ground Station in Hauppauge, NY
NSOF in Suitland, MD
3. ABI L1b, Space Wx L1b, and GLM L2 downlinked via GRB to NSOF or downlinked via GRB to NCEP Centers and Direct Readout Users.
NCEP Centers and Direct Readout Users
PDA Subscribers
6. SCMI (L2) and some L2+ products uplinked to a communications satellite.
7b. SCMI (L2) and L2+ products sent over SBN to external users.
NOAAPort Users
7a. SCMI (L2) and L2+ sent over SBN (o WFOs and RFCs
Weather Forecast Offices and River Forecast Centers
AWIPS Data Delivery will pull L2+ products from PDA at NSOF and send to each WFO/RFC on an ad-hoc and supplemental basis.
SES-1 communication satellite
Radiofrequency Transmission
4. L2+ products generated at NSOF and sent via PDA either to subscribers or to NCF for NWS distribution. PDA also distributes ABI L1b, Space Wx L1b, and GLM L2 products
Terrestrial Line
Notes: WCDAS – Wallops Command and Data Acquisition Station
NSOF – NOAA Satellite Operations Facility
SCMI – Sectorized Cloud and Moisture Imagery

## Slide 9: GRB
1. Raw data packets downlinked to WCDAS
At WCDAS, geometric and radiometric data added to L0 which processes L0 to L1b. Also, SCMI created and GLM L2.
2a. ABI L1b, Space Wx L1b, and GLM L2 uplinked to GOES-R via GRB.
WCDAS in Wallops, VA
NSOF in Suitland, MD
3. ABI L1b, Space Wx L1b, and GLM L2 downlinked via GRB to NSOF or downlinked via GRB to NCEP Centers and Direct Readout Users.
GRB users include all NCEP centers and direct readout users (i.e. anyone with a GRB antenna)
Data via GRB is ABI L1b, Space Weather L1b, GLM L2
NSOF receives GRB and generates the rest of the baseline (Level 2) products
NCEP Centers and Direct Readout Users
2b. SCMI (L2) sent to NCF through terrestrial line.
AWIPS Network Control Facility (NCF) in Silver Spring, MD
Notes: Talk about SCMI generation and flowing from Wallops to Silver Spring.

## Slide 10: PDA
5. SCMI (L2) and some L2+ products sent to Master Ground Station via terrestrial line.
Master Ground Station in Hauppauge, NY
NSOF in Suitland, MD
NOAAPort Users
Radiofrequency Transmission
Terrestrial Line
PDA users include anyone with a subscription.
PDA distributes all baseline products (ABI L1b, ABI L2+, Space Weather L1b, GLM L2). What you receive depends on your subscription.
4. L2+ products generated at NSOF and sent via PDA either to subscribers or to NCF for NWS distribution. PDA also distributes ABI L1b, Space Wx L1b, and GLM L2 products
AWIPS Network Control Facility (NCF) in Silver Spring, MD
7b. SCMI (L2) and L2+ products sent over SBN to external users.
7a. SCMI (L2) and L2+ sent over SBN (o WFOs and RFCs
SES-1 communication satellite
PDA Subscribers
Weather Forecast Offices and River Forecast Centers
AWIPS Data Delivery will pull L2+ products from PDA at NSOF and send to each WFO/RFC on an ad-hoc and supplemental basis.
6. SCMI (L2) and some L2+ products uplinked to a communications satellite.

## Slide 11: PDA Continued
There is NO backup for PDA if NSOF fails
HRIT/EMWIN rebroadcasts some data from PDA (exact products have not been finalized)
CLASS is populated with data from PDA

## Slide 12: Contingency Operations – WCDAS Failure
1. Raw data packets downlinked to CBU.
2a. ABI L1b, Space Wx L1b, and GLM L2 uplinked to GOES-R via GRB.
2b. SCMI (L2) sent to NCF through terrestrial line.
5. SCMI (L2) and some L2+ products sent to Master Ground Station via terrestrial line.
Master Ground Station in Hauppauge, NY
NSOF in Suitland, MD
3. ABI L1b, Space Wx L1b, and GLM L2 downlinked via GRB to NSOF or downlinked via GRB to NCEP Centers and Direct Readout Users.
NOAAPort Users
Radiofrequency Transmission
Terrestrial Line
4. L2+ products generated at NSOF and sent via PDA either to subscribers or to NCF for NWS distribution. PDA also distributes ABI L1b, Space Wx L1b, and GLM L2 products
AWIPS Network Control Facility (NCF) in Silver Spring, MD
7b. SCMI (L2) and L2+ products sent over SBN to external users.
7a. SCMI (L2) and L2+ sent over SBN (o WFOs and RFCs
SES-1 communication satellite
PDA Subscribers
Weather Forecast Offices and River Forecast Centers
AWIPS Data Delivery will pull L2+ products from PDA at NSOF and send to each WFO/RFC on an ad-hoc and supplemental basis.
NCEP Centers and Direct Readout Users
At CBU, geometric and radiometric data added to L0 which processes L0 to L1b. Also, SCMI created and GLM L2.
CBU in Fairmont, WV
6. SCMI (L2) and some L2+ products uplinked to a communications satellite.
Notes: CBU – Consolidated Backup Unit

## Slide 13: Contingency Operations – NSOF Failure
1. Raw data packets downlinked to WCDAS
At WCDAS, geometric and radiometric data added to L0 which processes L0 to L1b. Also, SCMI created and GLM L2.
2a. ABI L1b, Space Wx L1b, and GLM L2 uplinked to GOES-R via GRB.
2b. SCMI (L2) sent to NCF through terrestrial line.
5. SCMI (L2) and some L2+ products sent to Master Ground Station via terrestrial line.
Master Ground Station in Hauppauge, NY
NOAAPort Users
Radiofrequency Transmission
Terrestrial Line
AWIPS Network Control Facility (NCF) in Silver Spring, MD
WCDAS in Wallops, VA
7b. SCMI (L2) and L2+ products sent over SBN to external users.
7a. SCMI (L2) and L2+ sent over SBN (o WFOs and RFCs
SES-1 communication satellite
3. ABI L1b, Space Wx L1b, and GLM L2 downlinked via GRB to NSOF or downlinked via GRB to NCEP Centers and Direct Readout Users.
NCEP Centers and Direct Readout Users
Weather Forecast Offices and River Forecast Centers
6. SCMI (L2) and some L2+ products uplinked to a communications satellite.
Notes: No GOES-R to PDA interface at CBU.

## Slide 14: Outreach
AMS (American Meteorological Society) Broadcast Meteorology – June
Satellite Proving Ground OCONUS – July
AMS Satellite Meteorology – August
NWA (National Weather Association) Annual Meeting – Sept
EUMETSAT Annual Meeting – September
AMS Annual Meeting – January, 2017

## Slide 15: Questions?
Thank you to Eric Guillot and Bill Campbell of TOWR-S and Maurice McHugh of GOES-R/PDA