## Slide 1: Satellite Products Dissemination Christine Brunner NOAA/NWS Office of Dissemination May 10, 2016 2016 Satellite Proving Ground/User-Readiness Meeting

## Slide 2: Satellite Products Dissemination
  NWS IDP Ground Readiness Projects
    Background
    NOAAPort/SBN Expansion
    NWS GRB/H8 Antenna Project
    GOES-R NWS Posture
    NWS Network Projects
      Near-Term CONUS and OCONUS Projects
      Long-Term
Topics
2016 Satellite Proving Ground/User-Readiness Meeting

## Slide 3
Scope of this Presentation
      The primary emphasis of this presentation is on the dissemination of satellite products into and within NWS.
        In particular, this talk’s emphasis is on network and system upgrades taking place within (or in conjunction with) the NOAA Integrated Dissemination Program’s Ground Readiness Project (IDP/GRP). These projects reside principally within the NWS Dissemination Portfolio.

## Slide 4
Satellite data products use various networks to reach NWS users
SBN
  NWS users include WFOs, RFCs and National Centers (NCEP)
  Provides GOES-R imagery (Sectorized Cloud and Moisture Imagery or SCMI) to the AWIPS users (WFOs, RFCs, and National Centers)
  Routinely needed satellite products are delivered to NWS users through standing subscriptions
GOES-R Re-Broadcast (GRB) and HimawariCast antenna systems
  Installed at National Centers and certain OCONUS sites
  Provide them with the capability to produce their own imagery, lightning and space weather products
Terrestrial networks (OneNWS network)
  The OneNWS network is all encompassing network that will be sweeping up all existing NWS networks, providing more bandwidth, resiliency and end-to-end seamless management

## Slide 5
5
SBN Channels Carrying Satellite Products
Channel Name | Satellite Products | Example Products
NMC/NWSTG |  | GOES/Polar Soundings and GOES H.D. Winds* Radar, GRIB1 Grids, Watches/Warnings**
GOES/GINI |  | Legacy GOES Imagery (Mostly CONUS)
GOES-R West |  | GOES-R ABI Imagery (West)
GOES-R East |  | GOES-R ABI Imagery (East)
NMC2/NWSTG2 |  | GRIB2 model/analysis/forecast grids
OCONUS |  | GRIB1 OCONUS Grids, Legacy OCONUS GOES Imagery, DCS
POLARSAT |  | S-NPP/JPSS VIIRS Imagery
AWIPS Data Del. |  | Shared Subscription data
Experimental/Test |  | Test or Experimental Products: e.g. Total Precipitable Water, Cloud Top Height, Sea Surface Temperature, etc.
* Black font: Satellite products
** Grey font: Non-satellite products

## Slide 6
NWS GRB/Himawari Direct-Readout Antenna Project
Planned GOES-R/H8 Antenna Sites |  |  |  | 
NWS Office | East | West | Spare | Himawari
Alaska Region HQ* (Anchorage, AK) |  |  |  | 
Aviation Weather Center* (Kansas City, MO) |  |  |  | 
National Hurricane Center* (Miami, FL) |  |  |  | 
Pacific Region HQ* (Honolulu, HI) |  |  |  | 
Space Weather Prediction Center* (Boulder, CO) |  Q3 FY 2016 |  Q3 FY 2016 |  Q3 FY 2016 | 
Storm Prediction Center* (Norman, OK) |  |  |  | 
NOAA Center for Weather and Climate Prediction (College Park, MD) |  Q4 FY 2016 |  Q4 FY 2016 |  Q4 FY 2016 | 
Weather Forecast Office, Guam (Barrigada, GU) |  |  |  | 
NWS Sites Receiving Passive, Receive-only GOES-R/Himawari Antennas (Some spare antennas not shown).
*Existing GOES Antenna Site
 Antenna Installation Complete
Antenna Installation Underway/Planned
GRB and HimawariCast antenna installation completed at 6 of 8 sites
SWPC GRB antenna installation due to be completed by May 13, 2016 (next week)

## Slide 7
NWS GRB/Himawari Direct-Readout Antenna Project
SPC
Storm Prediction Center
Norman, OK
NHC
National Hurricane Center
Miami, FL

## Slide 8
OneNWS Terrestrial Network
WFO/RFCs
National Centers
All Centers have implemented WAN upgrades
Co-located offices to be transitioned to National Center WAN
All sites have implemented internet upgrades
Capacity upgrades in progress to bring to 100 Mbps (WFO) or 300 Mbps (WFO/RFC)
Office of Dissemination has received price quotes, orders currently being placed
The OneNWS Network project will enhance the NWS terrestrial networks by:
  OneNWS Network will simplify and improve management of NWS networks by consolidating regional networks under a single management structure
  Adding network capacity to the NWS WFOs, RFCs, Regional Headquarters and National Centers
  Ongoing discussions to define network solution for Regional Headquarters
  Provide physical diversity (physical redundancy) thus improving network resilience and reliability, subject to budget constraints
OCONUS
All networks upgraded with ample bandwidth
Physical diversity completed
Operational traffic migrated to new circuits
Legacy circuits being disconnected

## Slide 9: To-Be One-NWS Network: Access Layer
One-NWS Network MPLS
Vz PE
Vz PE
Vz PE
Vz PE
100 Mbps
100 Mbps
NEXRAD
LAN
WFO
Regional
LAN
AWIPS
LAN
HOT
STBY
NEXRAD
LAN
Co-located
WFO/RFC
Regional
LAN
AWIPS
LAN
HOT
STBY
RFC
LAN
300 Mbps
300 Mbps
RHQ
LAN
HOT
STBY
RHQ DMZ
Business Systems
Others
Regional HQ
TBD Mbps
TBD Mbps
Internet
DOC
TICAP
DOC
TICAP
Vz PE
Vz PE

## Slide 10
Long-Term “OneNWS Network” Project

## Slide 11
BACK-UP

## Slide 12
Himawari Full-Resolution Processing and Data Flows