## Slide 1
High Resolution Trajectory-Based Smoke Forecasts of the Fort McMurray wildfire using VIIRS Aerosol Optical Depth
JPSS Proving Ground and Risk Reduction Fire and Smoke Initiative
Brad Pierce
NOAA/NESDIS/STAR

## Slide 2
  Goal: Provide low latency, web-based, high resolution forecasts of smoke dispersion for use by NWS Incident Meteorologists (IMET) to support on-site decision support services for fire incident management teams.
  Project utilizes VIIRS AOD retrievals to initialize trajectory-based, high spatial resolution smoke dispersion forecasts.
  Project is an extension of Infusion of satellite Data into Environmental Applications-International (IDEA-I) trajectory based aerosol forecast capabilities and will be tested and released within CSPP prior to transition to Operations at NESDIS.

## Slide 3
Canadian Wildfires
May 04, 2016
Fort McMurray Wildfire

## Slide 4
IDEA-I High resolution (NAM 3km) trajectory forecast
Fort McMurray Wildfire
May 04, 2016
IDEA-I high resolution trajectories initialized at each 6km VIIRS pixel (only AOD>0.5 initialized)
Upper panel shows NAM 600mb heights
Lower panels show longitude and latitude cross sections
IDEA-I high resolution trajectory forecast colored by initial AOD

## Slide 5
IDEA-I High resolution (NAM 3km) trajectory forecast
Fort McMurray Wildfire
23Z May 05, 2016
Madison, WI
May 05, 2016 AERONET AOD shows plume over Madison, WI at 23Z
IDEA-I high resolution trajectory forecast captures observed arrival very well and shows that the plume is aloft.

## Slide 6
23Z May 05, 2016
US EPA AIRNow Observed (black) and RAQMS (red) analyzed PM2.5

## Slide 7
Canadian Wildfires
May 06, 2016

## Slide 9
652 WWUS83 KMPX 070627 SPSMPX SPECIAL WEATHER STATEMENT NATIONAL WEATHER SERVICE TWIN CITIES/CHANHASSEN MN 127 AM CDT SAT MAY 7 2016 MNZ042>045-049>053-058>063-066>070-075>078-071100- TODD-MORRISON-MILLE LACS-KANABEC-STEARNS-BENTON-SHERBURNE-ISANTI- CHISAGO-MEEKER-WRIGHT-HENNEPIN-ANOKA-RAMSEY-WASHINGTON-MCLEOD- SIBLEY-CARVER-SCOTT-DAKOTA-NICOLLET-LE SUEUR-RICE-GOODHUE- INCLUDING THE CITIES OF...LONG PRAIRIE...LITTLE FALLS... PRINCETON...MORA...ST CLOUD...FOLEY...ELK RIVER...CAMBRIDGE... CENTER CITY...LITCHFIELD...MONTICELLO...MINNEAPOLIS...BLAINE... ST PAUL...STILLWATER...HUTCHINSON...GAYLORD...CHASKA...SHAKOPEE... HASTINGS...ST PETER...LE SUEUR...FARIBAULT...RED WING 127 AM CDT SAT MAY 7 2016 ...SMOKY CONDITIONS TO PERSIST THROUGH THE OVERNIGHT HOURS... WIDESPREAD SMOKE FROM BOTH THE LARGE CANADIAN WILDFIRES AND A SMALLER WILDFIRE NEAR LAKE HATTIE IN HUBBARD COUNTY MINNESOTA HAS BLOWN INTO CENTRAL MINNESOTA...PARTICULARLY WITHIN AND NEAR THE TWIN CITIES METROPOLITAN AREA...DUE TO STRONG WINDS FROM THE NORTHWEST. VISIBILITIES HAVE BEEN REDUCED TO BETWEEN 1 AND 3 MILES...AND AIR QUALITY HAS BEEN SIGNIFICANTLY IMPACTED. THE SMOKE WILL LIKELY LAST THROUGH THE OVERNIGHT HOURS. LIMIT OUTDOOR ACTIVITIES TO PREVENT INHALING THE POOR QUALITY AIR. KEEP WINDOWS CLOSED TO LIMIT INTAKE INTO HOMES AND BUSINESSES.
From Andy Edman/NWS

## Slide 10
May 07, 2016
http://www.star.nesdis.noaa.gov/smcd/spb/aq/expr/expr2/

## Slide 11
https://www.airnow.gov/

## Slide 12
12Z May 07, 2016
US EPA AIRNow Observed (black) and RAQMS (red) analyzed PM2.5
12Z May 07, 2016
12Z May 07, 2016
12Z May 07, 2016