## Slide 1
The Advanced Baseline Imager (ABI) on the GOES-R Series
  Timothy J. Schmit (tim.j.schmit@noaa.gov) (“GOESguy”)
NOAA/NESDIS/Satellite Applications and Research
Advanced Satellite Products Branch (ASPB)
Madison, WI
  Plus many, many more…
UW-Madison
GOES-R Teachers Workshop
Cape Canaveral, FL
November 2016

## Slide 2: Thanks to…
Jordan Gerth
Scott Lindstrom
Kathleen Strabala
Bill Line
SSEC data center
Mat Gunshor
Scott Bachmeier
Kaba Bah
Steve Miller
Dan Lindsey
Steve Goodman
Chris Schmidt
Chad Gravelle
JMA
SSEC Real Earth team
ITT / Harris
Lockheed-Martin
Entire GOES-R team!
Dave Jones
COMET
You.

## Slide 3: Outline
Lockheed Martin
Introduction
  GOES and AHI
GOES-R ABI
  Spectral
  Spatial
  Temporal
  Derived Products
Summary

## Slide 4: NOAA GOES Constellation
GOES-16 or -17
(137W)
GOES-16 or -17
(75W)
After GOES-R and -S are launched, checked out & operational.
Notes: Template footer obscured. Fixed.
Estimate during mid-2010.

## Slide 5: Advanced Himawari Imagery (AHI)
Image is courtesy of Mitsubishi Electric.
Japan’s AHI launched:
  7 October 2014
Operational:
  02 UTC on 7 July 2015
Very similar to the ABI
  15 of the 16 spectral bands
Imager built by same company:
  Harris Corporation, Space and Intelligence Systems

## Slide 6
AHI Band | AHI Approximate Central Wavelength (μm) | ABI Approximate Central Wavelength (μm) | ABI Band | Type | Nickname
1 | 0.47 | 0.47 | 1 | Visible | Blue
2 | 0.51 |  |  | Visible | Green
3 | 0.64 | 0.64 | 2 | Visible | Red
4 | 0.86 | 0.86 | 3 | Near-Infrared | Veggie
 |  | 1.4 | 4 | Near-Infrared | Cirrus
5 | 1.6 | 1.6 | 5 | Near-Infrared | Snow/Ice
6 | 2.3 | 2.2 | 6 | Near-Infrared | Cloud Particle Size
7 | 3.9 | 3.9 | 7 | Infrared | Shortwave Window
8 | 6.2 | 6.2 | 8 | Infrared | Upper-level Water Vapor
9 | 6.9 | 6.9 | 9 | Infrared | Mid-level Water Vapor
10 | 7.3 | 7.3 | 10 | Infrared | Lower-level Water Vapor
11 | 8.6 | 8.4 | 11 | Infrared | Cloud-Top Phase
12 | 9.6 | 9.6 | 12 | Infrared | Ozone
13 | 10.4 | 10.3 | 13 | Infrared | “Clean” Longwave Window
14 | 11.2 | 11.2 | 14 | Infrared | Longwave Window
15 | 12.4 | 12.3 | 15 | Infrared | “Dirty” Longwave Window
16 | 13.3 | 13.3 | 16 | Infrared | CO2 Longwave
Advanced Baseline Imager Bands
Advanced Himawari Imager (AHI)

## Slide 7
AHI: Champi
(spectral bands)
Notes: Animation.

## Slide 8
GOES-R Advanced Baseline Imager (ABI)
  Spectral
    Improved!
  Spatial
    Improved!
  Temporal
    Improved!
Lockheed Martin

## Slide 9
ABI Band | Wavelength (µm) | Wavelength range (µm) | Sub-point pixel spacing (km) | Descriptive Name
1 | 0.47 | 0.45 - 0.49 | 1 | “Blue”
2 | 0.64 | 0.60 - 0.68 | 0.5 | “Red”
3 | 0.864 | 0.847 - 0.882 | 1 | “Veggie”
4 | 1.373 | 1.366 - 1.380 | 2 | “Cirrus”
5 | 1.61 | 1.59 - 1.63 | 1 | “Snow/Ice”
6 | 2.24 | 2.22 -2.27 | 2 | “Cloud Particle Size”
ABI: Bands 1-6 (Visible / NearIR)
Six visible or near visible bands on ABI, one on heritage imager
Notes: Based on Schmit et al, 2017. stars = today’s imager band.

## Slide 10
ABI Band | Wavelength (µm) | Wavelength range (µm) | Sub-point pixel spacing (km) | Descriptive Name
7 | 3.90 | 3.80 - 3.99 | 2 | “Shortwave window”
8 | 6.19 | 5.79 - 6.59 | 2 | “Upper-level Water Vapor”
9 | 6.93 | 6.72 - 7.14 | 2 | “Mid-Level Water Vapor”
10 | 7.34 | 7.24 - 7.43 | 2 | “Lower/Mid-level Water Vapor”
11 | 8.44 | 8.23 - 8.66 | 2 | “Cloud-top Phase”
12 | 9.61 | 9.42 - 9.80 | 2 | “Ozone”
13 | 10.33 | 10.18 - 10.48 | 2 | “Clean longwave window”
14 | 11.21 | 10.82 - 11.60 | 2 | “Longwave window”
15 | 12.29 | 11.83 - 12.75 | 2 | “Dirty longwave window”
16 | 13.28 | 12.99 - 13.56 | 2 | “CO2”
ABI: Bands 7-16 (Infrared)
10 infrared bands on the ABI, four on heritage imager
Notes: Based on Schmit et al, 2017. stars = today’s imager band.

## Slide 11: Current GOES Spectral Bands (5)
VIS
NIR
WV
IRW
CO2
1 Visible
0 Near-IR
4 IR

## Slide 12: ABI Spectral Bands (16)
0.64 m
0.86 m
1.38 m
1.61 m
2.26 m
3.9 m
6.19 m
6.95 m
7.34 m
0.47 m
8.5 m
9.61 m
10.35 m
11.2 m
12.3 m
13.3 m
2 Visible
4 Near-IR
10 IR

## Slide 13: ABI Spectral Bands
Visible
Near-IR

## Slide 14: ABI Spectral Bands (IR)

## Slide 15: Future vs. Current Spectral Bands
The current GOES (right) has 5 spectral bands, while the GOES-R series ABI (left) will have 16 spectral bands.
Notes: Animation.

## Slide 16: Baseline ABI Scan Modes
Scan mode (3) or ‘flex mode’ for the ABI:
- Full disk 15 minutes + 5 min CONUS + 1-min mesoscales (2 locations).
[Scan mode (4) or ‘Continuous Full Disk’ (CFD) is a full disk every 5 min]
Notes: CONUS image is the shifted center point.

## Slide 17
Meso-scale box locations are movable
15 min
5 min
1 min
1 min
Central
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-Test location. PUG CONUS sector. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 18
Proposed Default Meso Locations
For both West and East satellite locations

## Slide 19: ABI Scan Strategy
Concept of the ABI “flex mode” diagram
(image fades with time)
Full
Disk
Meso
CONUS
Meso
Time->

## Slide 20: Flex Mode Concept
Notes: Animation.

## Slide 21
MTSAT and AHI (visible band)
Approximate spatial resolution: 0.5 km
Approximate spatial resolution: 1 km
Notes: Images made with McIDAS-V by M. Gunshor, using a ‘square root’ enhancement. McIDAS-V

## Slide 22
Current GOES and GOES-R ABI
Simulation of Grand Prix Fire/Southern California
GOES-12
GOES-12
GOES-R ABI
GOES-R ABI
Notes: Here are two different fires from J. Feltz of CIMSS (using mcidas-v). What we can see is a more defined peak in the higher resolution data and it is easier to pick out individual hotspots. In addition, the higher saturation temperature of the ABI allows us to see that the fire is around 370K. ABI is simulated from MODIS.

## Slide 23
Note the improved spatial resolution from the AHI. There is evidence of waves over northern Japan in the AHI image, but not in the MTSAT image.
MTSAT vapor band
JMA’s AHI water vapor band centered at 7.0 μm
Notes: native projection. Both images are from July 7, 2015 at approximately 0330 UTC.

## Slide 24
What’s this infrared image showing?
Rinjani
?
?
?
?
?
Clouds
Arc clouds
Plume
Hot spot
Land
?
Cooler
Improved spatial resolution of an advanced imager
MTSAT
(older generation)
AHI
(new generation)
Notes: MTSAT vs AHI (Spatial) Plume is volcanic ash from Rinjani. Data from JMA, via STAR and the SSEC Data Center.

## Slide 25
GOES
Figure courtesy of K. Bedka and W. Feltz

## Slide 26
“ABI” from MODIS
Figure courtesy of K. Bedka and W. Feltz

## Slide 27: Advanced Baseline Imager (ABI)
5
4
3
X
Faster coverage (5-minute full disk vs. 25-minute)
X
Improved spatial resolution
(2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5 on the current imager)
ABI on GOES-S
Notes: Slide from J. Gerth, CIMSS.

## Slide 28
0.64 mm
3.9 mm
6.2 mm
13.3 mm
10.3 mm
11.2 mm
12.3 mm
6.9 mm
7.3 mm
8.4 mm
9.6 mm
0.47 mm
0.86 mm
1.37 mm
1.6 mm
2.2 mm
Simulated ABI Spectral bands during testing
GOES-R ABI Imagery simulated at UW-Madison via AWG Proxy, processed via the Ground System, acquired via NOAAPort, shown in AWIPS-II (default enhancements)
Notes: DOE-4