## Slide 1
45th Weather Squadron Weather Support to Launch
Kathy Winters
45th Weather Squadron
Launch Weather Officer
Notes: (This is a briefing to broadcast meteorologists that will be provided at an evening workshop on L-3)

## Slide 2
Overview
45th Weather Squadron
Weather Support to Launch
Primary Launch Vehicles
Hurricane Support
Pre-Launch Operations
Resource Protection
Weather Instrumentation
Launch Weather Support
  Upper Air Data
  Weather Launch Commit Criteria
  Launch Weather Team
  Weather Impacts to Launch
Notes: Overview of briefing

## Slide 3
Delta
Atlas
Trident
Falcon
3
Primary Range Users
“Exploit the Weather to Assure Safe Access to Air and Space”
Notes: Shown here are the primary launch vehicles we support
  When Space Launch is mentioned, most people probably think of the Space Shuttle, but we support an array of unmanned rockets.
This year we will reach about 21 launches by the end of December.

## Slide 4
4
GOES-R Mission
Notes: We were going to launch November 4th………

## Slide 5
5
But Wait….
Notes: But then Hurricane Matthew developed in the Caribbean…so the 45 WS provided hurricane support to ULA.
Daily updates, more frequent as the storm approached until we shut down and evacuated.
NHC Forecasts and what it means to us
Impacts to the Space Coast

## Slide 6
Hurricane Support Process
  45th Space Wing Commander and KSC Center
  Director Declare Hurricane Condition
  (HURCON) if Necessary
Tropical Cyclone Develops – 45 WS Monitors
  Listen to National Hurricane Center
  Conference Calls
  Send NHC Advisories to Customers
  Launch Weather Officers Provide Briefings
  to Launch Customers
Notes: During hurricane season, we monitor the tropics for the potential a tropical cyclone will threaten the Florida Spaceport
Our forecasters and Launch Weather Officers also listen to daily hurricane center discussions.
Launch Weather Officers brief the launch customers daily on the tropical activity.
If a storm develops, our squadron sends the NHC advisories to customers via Email, and we also post it on our web page.
If a storm becomes a threat to our the spaceport, our squadron commander informs the 45th Space Wing Commander. Our squadron also coordinates with the KSC Weather office and Emergency Managers who inform the KSC Center director.
The 45th Space Wing Commander and KSC Center Director will coordinate actions. Each will declare a hurricane condition if necessary.

## Slide 7
Hurricane Matthew, Category 4, 5 October
Notes: By Wednesday, 5 October, the NHC forecast for Matthew was rather bleak for the Space Coast, and the 45th Space Wing and it’s customers were preparing for a direct hit from a major hurricane.

## Slide 8
Hurricane Matthew, Category 3, 7 October
Notes: Hurricane Matthew skirted us just offshore from Cocoa Beach, with the outer-eye wall impacting the tip of the Cape and KSC. There was damage to facilities and ground support hardware.

## Slide 9
Hurricane Matthew, Wind Summary
Notes: Hurricane force winds impacted the coast.

## Slide 10
  Damage occurred to some facilities
Hurricane Matthew Recovery
Navaho Missile Display
Notes: We are often covering multiple pre-launch operations simultaneously. For example, the Delta IV WGS-8 mission was also accomplishing LVOS while the Atlas was.

## Slide 11
Booster Arrival and Offload, 9-10 October
Notes: Although Friday morning, 7 October, we were experiencing hurricane force winds, by Sunday, 9 October, the GOES-R was able to arrive at CCAFS Skid Strip on the Antonov aircraft.

## Slide 12
Launch Vehicle on Stand
Notes: After damage assessment and necessary repairs were complete, about a week later, it was time to get the launch vehicle to the Vertical Integration Facility. This includes the erection of the booster and the hoist and mate of the SRMs.
The Launch Weather Officer for the mission (Clay Flinn) provides detailed weather forecasts for this operation, focusing on the weather constraints for the operation. These constraints include lightning and wind.

## Slide 13
  Rockets & Payloads Being Readied at the Launch Pads Weeks to Months Before Launch
  5,000+ Ground Processing Operations per Year
Generation and Recovery
Notes: We are often covering multiple pre-launch operations simultaneously. For example, the Delta IV WGS-8 mission was also accomplishing LVOS while the Atlas was preparing to do the same.

## Slide 14
      Routine Daily Operations -- 24 / 7
Weather Warnings, Watches, Alerts, and Forecasts
  Safety for Over 25,000 People
  Resource Protection for Over $20 Billion Facilities
    Boosters / Payloads not Included (More $Billions)
  Lightning Alley of U.S.
    1,500+ Lightning Advisories per Year
Resource Protection
Notes: Because personnel and vehicle components are frequently exposed to the elements, our squadron provides a meteorological watch 24 hours a day, 7 days a week. Our forecasters issue weather watches, warnings, and advisories, and lightning watches and warnings are very specific to location so we can allow as much work to get accomplished as possible while keeping personnel and operations safe.

## Slide 15
World’s Most Diverse Mix Of Operational Weather Sensors
External Data Sources Too
Weather Instrumentation
Notes: We have a diverse set of instrumentation to assist with this forecasting, and also to help prevent exposing a vehicle to natural or triggered lightning during a launch.

## Slide 16
Weather Instrumentation
Notes: We have a vast spread of meteorological instrumentation across the space coast.

## Slide 17
Lightning Systems Especially Strong
Weather Instrumentation
WSR
WSR-88D
LPLWS
NLDN
WSR
MERLIN
WSR-88D/MLB
Notes: Our lightning systems are particularly robust. We have the MERLIN system which detects both in-cloud and cloud-to-ground lightning. We also have our own weather radar optimally configured for our operations, and we have access to the NWS’s Doppler weather radar as well. Our Field Mills are useful for Lightning Launch Commit Criteria evaluation.

## Slide 18
System
“Best Guess”
95% Confidence Ellipse
Lightning Stroke Information
Notes: Not only is forecasting lightning important, but letting our customers know if they had a nearby lightning stroke is also important. We provide daily lightning reports to our customers for any lightning strokes within 5NM of their key facilities. Given this data, the customer may determine their systems need to be tested before proceeding into operations to ensure there was no damage or induced current from a lightning stroke.

## Slide 19
Weather Support During Launch Week
  L-4, L-3, L-2, L-1 Day Forecasts with
  Probability of Weather Being No-Go
  Mission Dress Rehearsal
  Weather Briefings at Launch Readiness Reviews
  Press Briefings and Other Public Affairs Requests
  (Like this workshop briefing!)
Getting Closer to Launch
19

## Slide 20
Rollout
Vehicle Exposure
Notes: A day or two prior to launch, the GOES-R vehicle will be rolled out to the launch pad, away from the protection of the Vertical Integration Facility. During this time, exposure weather is forecast and monitored to ensure weather exposure constraints related to wind and lightning are not violated.

## Slide 21
Weather Impacts Other Launch Activities
User ‘LOADS’ Calculations
  Rocket Counter-Steering Against Upper-Level Winds can Destroy Itself
    Contractor Provides QC-ed Winds
    Evaluated by Engineering Community
Wing Safety -- Toxic Dispersion, Blast, Debris
Launch Operations
21
Shock Wave
Notes: About this time, we begin acquiring more Upper-air data which is used by the launch customers to evaluate aerodynamic loads on the vehicle during ascent to orbit. Also, range safety uses the data for evaluation of toxics, blast, and debris. We, the 45 Weather Squadron also use this data to assist in weather forecasting and also LLCC evaluation during the countdown.

## Slide 22
Launch Operations
Collect and Distribute Upper-Air Data
Notes: Balloon data is acquired to provide information to the launch customer concerning aerodynamic loads. Also, data from KSC’s Tropospheric Doppler Radar Wind Profiler is also used to compare to balloon data during editing and also reviewed by the launch customer as well.

## Slide 23
Launch Operations
Collect and Distribute Upper-Air Data
Notes: To ensure we can launch balloons with thunderstorms in the area, we worked with a local high school robotics team and NASA to obtain our Weather-Bot—developed by the “Pink Team”, this robot allows us to launch a balloon even when lightning is in the area. This can be an issue during a countdown if weather is moving through the area near the end of the countdown but clearing during the launch window.

## Slide 24
45 WS Forecasts and Evaluates Range Safety and User
Launch Commit Criteria
    Range Safety Launch Commit Criteria
      Lightning Launch Commit Criteria
        Rules to Avoid Natural &Triggered Lightning
        Constant for All Vehicles
      Ceiling / Visibility Constraints -- Varies by Vehicle
    User Launch Commit Criteria
      Lift-Off Winds, Temperature, Precipitation, Space Weather
      Varies by Vehicle and Vehicle Configuration
Weather Launch Commit Criteria
24
Notes: There are both range safety and user launch commit criteria. Range Safety criteria include the lightning launch commit criteria, and sometimes cloud ceiling and visibility criteria. The lightning launch commit criteria are the same for all vehicles. The ceiling and visibility criteria vary per vehicle.
The customers also have launch commit criteria which may include lift-off winds, flight through precipitation, temperatures, and even Space Weather. These are different for each launch vehicle.

## Slide 25
Natural Lightning: Produced by thunderstorms.
Triggered Lightning: Produced by aircraft and launch
vehicles under certain atmospheric conditions.
Triggered Lightning
Notes: Natural lightning is lightning that is occurring from a thunderstorm. We can easily detect this lightning and expect it from a thunderstorm. Triggered lightning is lightning that is generated by launching a rocket or flying an aircraft through an electric field that has built up. The path of the rocket disturbs the electrical field and provides the path of least resistance, triggering lightning.

## Slide 26
Lightning Launch Commit Criteria
Notes: After the Atlas-Centaur triggered lightning event in 1987, NASA funded a lightning advisory panel, a team of lightning experts from across the country. The team developed a new set of lightning launch commit criteria. This team is still in existence today, and updates the rules regularly, refining them to ensure safety while allowing as much launch availability as possible.
Let’s look at the Lightning rule as an example…. (click for animation to blow up lightning rule image…describe rule, note caveats)— this is a good example of complexity of the Lightning LCC. (This slide has an animation that brings out the lightning rule slide).

## Slide 27
Launch Weather Team
Tag Up
Launch
Weather Commander
Launch Weather Director
27
RECCE
Range Weather Forecaster
Radar
WX Bot
Complex Weather Launch Commit Criteria
Launch Weather Officer
Notes: The 45th Weather Squadron Launch Weather Team evaluates the Launch Commit Criteria. The Launch Weather Officer reports this criteria status to the Range and the User. If any Launch Weather Officer on the team is NO-GO, then the team is NO-GO. All Launch Weather Officer team members must agree to return to a GO status with final approval from the LWC. The team must be CLEARLY CONVINCED weather criteria are not violated to be GO.

## Slide 28
Launch
ULA Team
Launch Weather Team
Launch!
Range Team
Notes: We provide our status to the Range Team and also the ULA launch team– hopefully we are GO FOR LAUNCH!!!

## Slide 29
Weather Impacts to Launch
Notes: How often does weather impact launch? Almost 50% of scrubs are due to weather, and a quarter of countdowns are impacted by weather.

## Slide 30
Mission:“Exploit the weather to assure safe access to air and space”
45th Weather Squadron Team
Notes: I want to wrap this up with a photo of our 45th Weather Squadron team. From the time the vehicle components arrive to the time they launch (and possibly land), our team is ready to support all operations! We are a mix of military and civilians, with the military providing breadth of knowledge they bring from their experience at other locations, and the civilians providing depth of knowledge, being involved in a launch program for the long term. I am proud and lucky to be part of this amazing team!

## Slide 31
Questions?
Notes: Review latest launch forecast and then see if there are questions.