## Slide 1: Joint Polar Satellite System (JPSS) Instrument Calibration and Validation
Fuzhong Weng, JPSS SDR Science Chair
National Environmental Satellites, Data and Information Service
National Oceanic and Atmospheric Administration (NOAA)
Contributed by STAR JPSS SDR Leads: Yong Han, Changyong Cao, Larry Flynn, Ninghai Sun
SDR Principal Investigators: Hu Yang, Vince Leslie, Xiaolei Zou, Hank Rivercomb, Dave Tobin, Larrabee Strow, Dan Mooney, Deron Scott , Degui Gu, Jack Xiong, Frank Deluccia, Robert Wolfe, Glen Jaross , Chunhui Pan and many others

## Slide 2: Suomi NPP and JPSS-1 Instruments
Instrument Type |  | Measurement
 | ATMS - Advanced Technology Microwave Sounder | ATMS and CrIS together provide high vertical resolution temperature and water vapor information needed to maintain and improve forecast skill out to 5 to 7 days in advance for extreme weather events, including hurricanes and severe weather outbreaks
 | CrIS - Cross-track Infrared Sounder | 
 | VIIRS – Visible Infrared Imaging Radiometer Suite | VIIRS provides many critical imagery products including snow/ice cover, clouds, fog, aerosols, fire, smoke plumes, vegetation health, phytoplankton abundance/chlorophyll
 | OMPS - Ozone Mapping and Profiler Suite | Ozone spectrometers for monitoring ozone hole and recovery of stratospheric ozone and for UV index forecasts
 | CERES - Clouds and the Earth’s Radiant Energy System | Scanning radiometer which supports studies of Earth Radiation Budget
2

## Slide 3: Suomi NPP TDR/SDR Algorithm Schedule
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Sensor | Beta | Provisional | Validated
CrIS | February 10, 2012 | February 6, 2013 | March 18, 2014
ATMS | May 2, 2012 | February 12, 2013 | March 18, 2014
OMPS | March 7, 2012 | March 12, 2013 | April , 2015
VIIRS | May 2, 2012 | March 13, 2013 | April 16, 2014
Beta
Early release product.
Initial calibration applied
Minimally validated and may still contain significant errors (rapid changes can be expected. Version changes will not be identified as errors are corrected as on-orbit baseline is not established)
Available to allow users to gain familiarity with data formats and parameters
Product is not appropriate as the basis for quantitative scientific publications studies and applications
Provisional
Product quality may not be optimal
Incremental product improvements are still occurring as calibration parameters are adjusted with sensor on-orbit characterization (versions will be tracked)
General research community is encouraged to participate in the QA and validation of the product, but need to be aware that product validation and QA are ongoing
Users are urged to consult the SDR product status document prior to use of the data in publications
Ready for operational evaluation
Validated
On-orbit sensor performance characterized and calibration parameters adjusted accordingly
Ready for use in applications and scientific publications
There may be later improved versions
There will be strong versioning with documentation

## Slide 4: Suomi NPP Calibration/Validation Schedule
Four Phases of Cal/Val:
  Pre-Launch; all time prior to launch – Algorithm verification, sensor testing, and validation preparation
  Early Orbit Check-out (first 30-90 days) – System Calibration & Characterization
  Intensive Cal/Val (ICV); extending to approximately 24 months post-launch – xDR Validation
  Long-Term Monitoring (LTM); through life of sensors after ICV
For each phase:
  Exit Criteria established
  Activities summarized
  Products mature through phases independently
10-28-2011
12-18-2013 Validated Review
10-23-2012-Provisional Review
Joint Polar Satellite System

## Slide 5: NOAA Integrated CalVal System (ICVS) for Long Term Monitoring (LTM) of Operational Satellites
http://www.star.nesdis.noaa.gov/icvs

## Slide 6: SNPP Advanced Technology Microwave Sounder (ATMS) TDR/SDR Status
TDR/SDR data have reached a full validated maturity level
ATMS has a stable instrument performance and calibration
ATMS instrument noises (NEDT) are characterized and all channels meet or exceed the requirements
All the ATMS channels have noises much lower than specification
ATMS processing coefficients table (PCT) are updated with nominal values
Quality flags (e.g. spacecraft maneuver and scanline, calibration) are updated and monitored
Geolocation errors for all the channels are quantified and meet specification
Instrument performance and SDR uncertainties are well characterized and documented (e.g. ATBD, peer-reviewed publications, user’s guide, error budget analysis)
Both TDR and SDR products are used in NOAA operations
Innovated sciences have been made for instrument calibration
Notes: NPP Satellite Acquires First ATMS Measurements The image shows the ATMS channel 18 data, which measures water vapor in the lower atmosphere. Tropical Storm Sean is visible in the data, as the patch of blue, in the Atlantic off the coast of the Southeastern United States.

## Slide 7
Ch | GHz | Pol | Ch | GHz | Pol | Ch | GHz | Pol
 |  |  | 1 | 23.8 | QV | 1 | 23.8 | QV
 |  |  | 2 | 31.399 | QV | 2 | 31.4 | QV
1 | 50.299 | QV | 3 | 50.299 | QV | 3 | 50.3 | QH
 |  |  |  |  |  | 4 | 51.76 | QH
 |  |  | 4 | 52.8 | QV | 5 | 52.8 | QH
2 | 53.74 | QH | 5 | 53.595 ± 0.115 | QH | 6 | 53.596 ± 0.115 | QH
 |  |  | 6 | 54.4 | QH | 7 | 54.4 | QH
3 | 54.96 | QH | 7 | 54.94 | QV | 8 | 54.94 | QH
 |  |  | 8 | 55.5 | QH | 9 | 55.5 | QH
4 | 57.95 | QH | 9 | fo = 57.29 | QH | 10 | fo = 57.29 | QH
 |  |  | 10 | fo ± 0.217 | QH | 11 | fo±0.3222±0.217 | QH
 |  |  | 11 | fo±0.3222±0.048 | QH | 12 | fo± 0.3222±0.048 | QH
 |  |  | 12 | fo ±0.3222±0.022 | QH | 13 | fo±0.3222±0.022 | QH
 |  |  | 13 | fo± 0.3222±0.010 | QH | 14 | fo±0.3222 ±0.010 | QH
 |  |  | 14 | fo±0.3222±0.0045 | QH | 15 | fo± 0.3222±0.0045 | QH
 |  |  | 15 | 89.0 | QV |  |  | 
 |  |  | 16 | 89.0 | QV | 16 | 88.2 | QV
 |  |  | 17 | 157.0 | QV | 17 | 165.5 | QH
 |  |  |  |  |  | 18 | 183.31 ± 7 | QH
 |  |  |  |  |  | 19 | 183.31 ± 4.5 | QH
 |  |  | 19 | 183.31 ± 3 | QH | 20 | 183.31 ± 3 | QH
 |  |  | 20 | 191.31 | QV | 21 | 183.31 ± 1.8 | QH
 |  |  | 18 | 183.31 ± 1 | QH | 22 | 183.31 ± 1 | QH
Exact match to AMSU/MHS
Only Polarization different
Unique Passband
Unique Passband, and Pol. different
from closest AMSU/MHS channels
AMSU/MHS
ATMS
MSU
Notes: An overview of the principal differences between ATMS and AMSU.

## Slide 8: ATMS Channel Weighting Functions
Pressure (hPa)
Weighting Function

## Slide 9: ATMS Noise Equivalent Differential Temperature (NEDT)
SNPP ATMS noise equivalent differential temperature (NEDT) from prelaunch and postlaunch data is much smaller than specification. Currently, the oversampling ATMS data (3x3) are re-sampled by users for noise reductions and the actual ATMS noises at the temperature sounding channels after resampling are much lower than the AMSU-A values.
NEΔT (K)
Channel Number

## Slide 10: Impacts of US Microwave Sounders in NCEP GFS 500 hPa Southern Hemisphere AC scores for 20140101 – 20140131 00Z
Assimilation of ATMS radiances in NCEP GFS produces a largest impact on global medium range forecast, especially over southern hemisphere. With respect to the baseline experiment that includes the conventional and GPSRO data, 75% forecast skill increase is attributed to ATMS radiance assimilation.

## Slide 11
Control Run
ATMS Impacts on Hurricane Sandy Forecast 2012 NCEP HWRF Version
Control Run +ATMS
Predicted vs. observed track for Hurricane Sandy during October 22 to 29. NCEP 2012 HWRF is revised with a high model top and is initialized with its own background 6 hour forecast for direct satellite radiance assimilation in GSI. Control Run: All conventional data and NOAA/METOP/EOS/COSMIC. It is clearly demonstrated that assimilation of Suomi NPP ATMS radiance data reduces the forecast errors of Hurricane Sandy’s track

## Slide 12: Atmospheric River Depicted from ATMS
Atmospheric water vapor retrieved from SNPP ATMS using NOAA microwave integrated retrieval system (MIRS). MIRS is developed for all US and European microwave sounding instruments and meets the enterprise product lifecycle standards (e.g. common interface, CRTM, JPSS L1RD performance).

## Slide 13
Warm Core - Temperature Anomaly Typhoon Neoguri 07/07/2014

## Slide 14
Biases in the Tropics (NOAA-15, MetOp-A, SNPP)
before
after
ATMS channel 10
ATMS channel 11
ATMS channel 13
ATMS channel 14
Bias (K)
Bias (K)
Bias (K)
Bias (K)
NOAA-18 is subtracted. The pentad data set within ±30o latitudinal band.

## Slide 15
Without LI correction
With LI correction
ATMS Lunar Intrusion Correction Algorithm
Brightness temperature increment arising from lunar contamination can be expressed as a function of lunar solid angle, antenna response and radiation from the Moon
Space view Tb or radiance increment:
Antenna response function:
Weights of the Moon in antenna pattern:
Brightness temperature of the Moon:

## Slide 16: New ATMS SDR Algorithm including Spill-over and Side-lobe Corrections
Weng, F., X. Zou, M. Tian, W.J. Blackwell, N. Sun, H. Yang, X. Wang, L. Lin, and K. Anderson, 2013, Calibration of Suomi National Polar-Orbiting Partnership (NPP) Advanced Technology Microwave Sounder (ATMS), J. Geophys. Res, 118, 1–14, doi:10.1002/jgrd.50840 ,
For Quasi-V (TDR) :
For Quasi-H (TDR)
Notes: For Microwave instrument, Observation is antenna temperature in which the antenna pattern effects are included. To derive the real earth scene temperature, the conversion from TDR to SDR are needed. ATMS measurements only include single polarization observation, to correct antenna pattern effects, measurements in another polarization need to be simulated.
公式改成radiance， Aq符号改正

## Slide 17: ATMS Polarization vs. Scan Angle
Scan Angle
Scan Angle
Scan Angle
Scan Angle
Scan Angle
Scan Angle
TB (K)
TB (K)
Ch1
Ch2
Ch3
Ch4
Ch16
Ch17
The brightness temperature with pure (dashed curve) and quasi- (solid curve) horizontal polarization (circle) and vertical (star) polarization states using the US standard atmospheric profile with sea surface wind speed being 5 m/s and sea surface temperature being 290 K.

## Slide 18: ATMS Resampling Algorithm using the Backus-Gilbert (BG) Method
(FOV)
(FOV)
Scanline
Scanline
ATMS Channels 3-16
ATMS Channels 1-2
An effective AMSU-A target FOV: output of BG remap (shaded in gray)
ATMS effective FOVs: Circles with colors indicating the magnitude of BG coefficients

## Slide 19: ATMS Resampling Algorithm
Stogryn, A., 1978: Estimates of brightness temperatures from scanning radiometer data. IEEE Trans. Ant. & Prop., AP-26, 720-726.

## Slide 20: Tb at Channel 1 within Sandy before and after Remap
(K)
(contour interval: 1K)
NCEP GFS SLP
(contour interval: 10hPa)
(original)
(0600 UTC October 28, 2012)
(after BG)

## Slide 21: SNPP Cross-Track Infrared Sounder (CRIS) SDR Status
CRIS SDR data have reached a full validated maturity level
On-orbit instrument performance is stable and well within specification
SDR uncertainties meet requirements, with NEdN and uncertainties of radiometric and spectral calibration well below specifications
Spectral uncertainty: < 3 ppm, well below specification
Radiometric uncertainty: ~0.1K, well below specification
Geolocation error: < 1.2 km below specification
ILS and NL correction algorithms/code and coefficients are improved and adjusted
All the important SDR quality flags are functioning as expected
99.98% of the SDR data are in good quality
IDPS capability to process full resolution RDRs is implemented and tested
Instrument performance and SDR uncertainties are well characterized and documented (e.g. ATBD, peer-reviewed publications, user’s guide, error budget analysis)
CrIS SDR team developed lots of innovative algorithms for full resolution SDR processing
Notes: NPP Satellite Acquires First ATMS Measurements The image shows the ATMS channel 18 data, which measures water vapor in the lower atmosphere. Tropical Storm Sean is visible in the data, as the patch of blue, in the Atlantic off the coast of the Southeastern United States.

## Slide 22: Example of Data Quality after Mx8.0
Radiance (900 cm-1)
Overall SDR quality flag (Blue – good)
  http://www.star.nesdis.noaa.gov/icvs/status_NPP_CrIS.php
CrIS data monitoring website:

## Slide 23: Validated CrIS SDR Product
Band | NEdN @287K BB mW/m2/sr/cm-1 | Radiometric Uncertainty @287K BB (%) | Frequency Uncertainty (ppm) | Geolocation Uncertainty (km) *
LW | 0.098 (0.14) | 0.12 (0.45) | 3 (10) | 1.2 (1.5)
MW | 0.036 (0.06) | 0.15(0.58) | 3 (10) | 1.2 (1.5)
SW | 0.003 (0.007) | 0.2 (0.77) | 3 (10) | 1.2 (1.5)
Requirements
  Instrument & SDR performances exceed requirements by large margins
SDR software
  Stable & free of errors that could impact data quality since 11/14/2013 (Mx8.0)
Documentation
  SDR User’s Guide (55 pages)
  Revised ATBD
  Peer-review Journal papers
CrIS SDR uncertainties (blue) vs. specifications (black)

## Slide 24
Note: MWIR7 (Green) is known to have excess NEdN (expected)
CrIS Noise Equivalent Differential Radiance (NEdN)
NEdN On-Orbit data is consistent with Ground Test Data (Black Lines); Much Better Than Spec Limits (Dashed Lines)………No Ice Contamination Signatures
Slide courtesy of Joe Predina, ITT EXELIS

## Slide 25: SNPP CrIS Full Spectral Resolution SDR Processing
SNPP CrIS has been switched to full spectral resolution (FSR) mode in November 2014
NOAA STAR prepared an offline processing system to provide FSR Sensor Data Records (SDRs) to the science community while NOAA CLASS will continue to distribute the normal resolution SDRs
New SDR data still keeps low noises although the resolution in SW and MW increases due to the fine tuning of calibration algorithms (e.g. CMO optimization)
All parameters (9 fov *1306+ancillary ) regarding CRIS RDR/SDR data quality, instrument telemetry/house keeping information are fully trended and monitored
CRIS full resolution data has produced a high quality of carbon/GHG products due to its low noise and high resolution.

## Slide 26
SNPP CrIS Full Spectral Resolution SDR
Frequency Band | Spectral Range (cm-1) | Number of Channel | Spectral Resolution (cm-1)
LWIR | 650 to 1095 | 713 (713) | 0.625 (0.625)
MWIR | 1210 to 1750 | 865 (433) | 0.625 (1.25)
SWIR | 2155 to 2550 | 633 (159) | 0.625 (2.5)
Red: Full resolution mode
CH4
CO
CO2

## Slide 27: SNPP Visible Infrared Imaging Radiometer Suite (VIIRS) SDR Status
VIIRS SDR products have reached a validated maturity level
Multiple code/LUT updates have been implemented or are being implemented into the SDR processing, including the scan-by-scan calibration, and have led to higher quality SDRs and EDRs.
VIIRS on-orbit performance is well characterized and meets specifications
Noise is small and stable, meet specification
Bias (accuracy) is well characterized for both reflective solar and thermal emissive bands. with the exception of M11 due to low signal (known prelaunch with waiver)
Calibration coefficients are automatically updated
RSB Autocal is implemented and reduce calibration latency and improve performance.
DNB straylight correction works well.
Geo-location uncertainties for I-/M-bands are ~ 70 m at nadir, meeting specifications at nadir and edge-of-scan (DNB terrain corrected geo-location product is expected in Mx8.3 in March 2014)
Instrument performance and SDR uncertainties are well characterized and documented (e.g. ATBD, peer-reviewed publications, user’s guide, error budget analysis)
Notes: Early on August 28, 2012, the Visible Infrared Imaging Radiometer Suite (VIIRS) on the Suomi-NPP satellite captured this nighttime view of Tropical Storm Isaac and the cities near the Gulf Coast of the United States. The image was acquired just after local midnight by the VIIRS “day-night band,” which detects light in a range of wavelengths from green to near-infrared and uses light intensification to enable the detection of dim signals. In this case, the clouds of Isaac were lit by moonlight.

## Slide 28: VIIRS SDR Accuracy
 | Requirement (absolute uncertainty for uniform scenes) | Prelaunch and onboard calibration | Validation: Relative to MODIS/CrIS/IASI/other thru Inter-comparisons | Note
VIIRS RSB | 2% typical reflectance; 0.3% stability; 0.1% desirable for Ocean Color Applications | 1.2% for M1-M7; 1.5% for M8&9 1.4% for M10 1.3% for I1&I2 1.6% for I3 | 2% (±1%) for matching bands | Except bands with very low signal (ex. M11) Geolocation error: expectation is half I-band pixel; achieved better than quarter I-band pixel (1-s)
VIIRS TEB | M12/M13: 0.7%(0.13K) @270K M14: 0.6% (0.26K) @ 270K M15/M16: 0.4% (0.22K/0.24K) @270K I4: 5% (0.97K) @270K I5: 2.5% (1.5K) @270K | Better than 0.13K for all M bands except M13 (0.14); 0.47K for I4; 0.23K for I5 | 0.1K based on statistical comparison with MODIS and CrIS ER-2/SHIS Aircraft underflight shows excellent agreement M15 0.4 K bias relative to CrIS at 200K (in spec.) | M15 at 190K requirement is 2.1% radiance or 0.56K Geolocation uncertainty: expectation was half I-band pixel; achieved better than quarter I-band pixel (1-s)
VIIRS DNB | 5%, 10%,30% Lmin (LGS,MGS,HGS) | 3.5%, 7.8%, and 11% (LGS, MGS, HGS) | 4%, 7.7%, 11.8% (LGS, MGS, HGS) | Geolocation error is a ~10th of a pixel (1-s) on the ellipsoid earth but can exceed 1km (up to 24 km at the edges of scan) without terrain correction

## Slide 29: VIIRS On-orbit Performance -SNR and NEDT (all values are stable since provisional)
Excellent noise performance for all VIIRS bands
Noise values stable since launch

## Slide 30: VIIRS Reflective Solar Band (RSB) Calibration
F: RSB Calibration coefficient.
H: SD degradation factor.
dn: VIIRS bias removed response
dc: SDSM bias removed response

## Slide 31: VIIRS RTA and Solar Diffuser Degradation
VIIRS RTA mirror responsivity degradation (1/F-factor) is leveling off
For M7, initially > 2% per week; Currently <0.1% per week
Solar diffuser (1/H-factor) degradation continues
Both H and F factor degradation flattened in the spring of 2014, which disrupted the trend. As a result, the calibration model has to be revised
Automated calibration of the solar bands using the “RSB Autocal” is currently being tested

## Slide 32: VIIRS Performance at 30 Vicarious Sites Worldwide
Nadir
VIIRS calibration is monitored at 30 Vicarious sites with time series analysis for all bands
DCC and Lunar are recognized as a unique sites and have been used to diagnose calibration anomalies
The DCC time series are capable of detecting sub-percent calibration changes.
  Bands M5 and M7 are stable, with calibration of stability better than 0.4% (1-sigma);
  Bands M1-M3 show noticeable calibration changes, especially since early 2014, due to the SD anomaly
Time series available at: https://cs.star.nesdis.noaa.gov/NCC/VSTS.
Feb 2014
VIIRS DCC observation time series
30 vicarious sites for VIIRS calibration monitoring

## Slide 33: SNPP Ozone Mapping and Profiling Suite (OMPS) SDR Status
OMPS Earth View SDR products have reached a validated maturity level
Excellent OMPS instrument performance, as validated by STAR ICVS monitoring.
Calibration coefficients have been adequately updated.
OMPS and GOME-2 inter-sensor biases are well characterized. Good agreements with existing knowledge of GOME-2 calibration.
Excellent outreach to and feedback from NOAA and NASA user community.
OMPS SDR on-orbit performance is well characterized. Exceptional performance in terms of noise, stability, and data completeness.
Further improvements in stray light correction is being implemented. Current performance meets requirements.
A new wavelength correction is being implemented, after which performance will meet requirements.
Need a plan to correct for wavelength cross-track variation, e.g. by improved pixel-to-pixel cal. in scan direction or soft cal.
Good documentation in peer-reviewed papers and presentations for this review.

## Slide 34: OMPS Scanning Characteristics
OMPS consists of three spectrometers
  Nadir Total Column Spectrometer covers a 50km x 2800km cross-track swath
  Nadir Profile Spectrometer provides performance over (250km)2 cell
  Limb Sensor provides 1 km vertical sampling along three slits enabling ozone profile retrieval (Not on J1)
PFM PSR completed Nov ’08
Heritage: TOMS (Nadir Total Column) and SBUV/2 (Nadir Profiler)

## Slide 35
Table Description | Table Type | Delivery Status
NM & NP Solar Flux | LUT | Once (will be repeat )
NM & NP Wavelength | GND-PI | Once (will be repeat )
NM & NP CF Earth | GND-PI | When necessary
NM & NP Dark Tables | GND-PI | Weekly
Diagnostic Flight Sample Tables | SCT | When necessary
Earth-view Flight Sample Tables | SCT | Once
Earth-view Ground Sample Tables | GND-PI | Once
Calibration Flight Sample Tables | SCT | Once
NM & NP Radiometric Coefficients | LUT | TBD
NM Stray Light Coefficients | LUT | Once
NP Stray Light Coefficients | LUT | Once
NM & NP Linearity (Flight & Ground) | SCT/GND-PI | Not planned
NM & NP Flat Field | SCT | Not planned
OMPS SDR Calibration Table

## Slide 36: OMPS Nadir Mapper Instrument Performance
Requirement | Specification/Prediction Value | On-Orbit Performance
Non-linearity | < 2% full well | < 0.46%
Non-linearity Knowledge | < 0.5% | ~0.1%
On-orbit Wavelength Calibration | < 0.01 nm | 0.01 nm #
Stray Light NM Out-of-Band + Out-of-Field Response | ≤ 2% | average ~± 0.5% ^
Intra-Orbit Wavelength Stability | <0.02 nm | < 0.01 nm *
SNR | >1000 | > 1000 from SV and EV
Inter-Orbital Thermal Wavelength Shift | <0.02 nm | <0.01 nm
CCD Read Noise | <60 –e RMS | < 25 –e RMS
Detector Gain | >46 | ~51
Absolute Irradiance Calibration Accuracy | < 7% | <7% (< 8% on wavelengths <306 nm)
Absolute Radiance Calibration Accuracy | < 8% | < 5%
# After new analysis for Day 1 wavelength scale.
^ After measurement-based correction using prelaunch characterization.
* After measurement-based intra-orbit adjustments.
Notes: From SDR provisional presentation with new notes by L. Flynn.

## Slide 37: OMPS NP Instrument Performance
Requirement | Specification/Prediction Value | On-Orbit Performance
Non-linearity | < 2% full well | < 0.46%
Non-linearity Knowledge | < 0.5% | ~0.1%
On-orbit Wavelength Calibration | < 0.01 nm | < 0.01 nm #
Stray Light NM Out-of-Band + Out-of-Field Response | ≤ 2% | average ~± 1% *
Intra-Orbit Wavelength Stability | <0.02 nm | < 0.02 nm
SNR | Channel Dependent | As good as SBUV/2 at Alg. Channels &
Inter-Orbital Thermal Wavelength Shift | <0.02 nm | 0.03-nm amplitude annual cycle ^
CCD Read Noise | <60 –e RMS | < 25 –e RMS
Detector Gain | >43 | ~47
Absolute Irradiance Calibration Accuracy | < 7% | < 7% for most of the channels (Up to ~10% on wavelength s > 305 nm and wavelengths < 250 nm)
Absolute Radiance Calibration Accuracy | < 8% | < 5%
# After analysis of a new Day 1 Solar
* After measurement-based correction using prelaunch characterization
^ Regular annual cycle affects accuracy and stability
& Information concentration possible by using near-by channels.
Notes: From C. Pan SDR Provisional.
New notes from L. Flynn.

## Slide 38: JPSS-1 ATMS Status
J1 ATMS TVAC calibration data were provided to the government for independent assessment
  Testing performed for 4 redundancy configurations at each calibration step
  For each calibration step, 278 scans of data processed to yield 271 scans of derived accuracy data
Major findings from TVAC data
  Except Chs.16 and 17, the performances (accuracy, NEDT and nonlinearity) at all other channels meet the requirements
  Overall, redundancy configuration 1 (RC1) is recommended to use.
  To avoid the NEDT and striping abnormal in Ch.16, a higher (~ 13-14oC) instrument temperature could be considered to use.
J1 ATMS is now undergoing a rework and PSR will take place in August, 2015
J1 ATMS SDR algorithms will most inherit SNPP ATMS algorithms with some updated sciences. Calibration will be done in radiance space and the outputs will be converted to brightness temperature (see next slide)
JPSS ATMS Post Launch Tests (PLT) is being developed. J1 ATMS SDR data will be operational at L+90 Days.

## Slide 39: Analysis of ATMS TVAC Test Data
SNPP TVAC Data (RC1 230K)
J-1 TVAC Data (RC4, 3/12/14)
Preliminary TVAC data analysis shows J1 ATMS is much cleaner than SNPP, except channel 16 and 17.

## Slide 40: JPSS-1 ATMS SDR Upper Algorithms
Radiance calibration algorithm
Considering the error arose from R-J approximation, a full radiance calibration is adopted as the standard calibration method for both the two-point linear calibration and non-linear correction
An Advanced Radiance Transformation System (ARTS) is designed for microwave sounding instruments. With new sciences developed from solid study of SNPP ATMS, the calibration accuracy of TDR products from future JPSS satellite will be improved
μ parameter based nonlinearity correction algorithm
Maximum nonlinearity was expressed as function of μ parameter
Nonlinear parameter was expressed as function of instrument temperature for on-orbit nonlinearity correction
Reflector emissivity correction algorithm
full vector expression for reflection and transmission for non-lossless, polarized rotating reflector was developed.
physical model for antenna reflector emissivity correction was established
Lunar intrusion correction algorithm
LI is modeled as a function of antenna response, solid angle of the Moon and the microwave emission from the Moon
The new correction model with best fitted parameters from ATMS observations can effectively reduce the calibration error due to lunar contamination on cold counts
De-stripping algorithm
Based on power spectrum analysis, stripping index and de-striping algorithm was developed to reduce the flicker noise in calibration data and TDR products
The flicker noise and correlation on the JPSS1 ATMS is much lower than S-NPP ATMS
TDR Remapping algorithm
B-G algorithm was developed to explore the advantage of ATMS oversampling feature
By using B-G algorithm, remapping coefficients were generated offline, to remap ATMS observation to different FOV size

## Slide 41: JPSS-1 CrIS Status
  The PSR successfully completed on 10 February 2015
  Instrument environmental test campaign successfully completed
  Only one science-related waiver with negligible impact to Environmental Data Record (EDR) performance
  All program review actions are closed
  J1 CrIS is on the way to BATC for satellite level test campaigns
Cross-track Infrared Sounder (CrIS)

## Slide 42: JPSS-1 CrIS Upper SDR Software Delivered
J1 upper algorithms
  Process raw data into full spectral resolution sensor data records (SDRs) (2211 channels)
  Has the backward-compatibility to process raw data into the current normal resolution spectra (1305 channels)
J1 upper algorithm/software delivered on 15 January 2015
  Software has been tested since 4 December 2014 with the S-NPP full spectral resolution mode measurements
Δσ = 0.625 cm-1
Δσ = 0.625 cm-1
Δσ = 1.25 cm-1
Δσ = 0.625 cm-1
Δσ = 2.5 cm-1
Δσ = 0.625 cm-1
LW band
MW band
SW band
CrIS full (red) and normal (black) resolution spectra

## Slide 43: JPSS-1 VIIRS Status
J1 VIIRS Pre-Ship Review Review (PSR) was held 2/3-2/4 at Raytheon, El Segundo, CA
PSR provides a systematic review of the instrument, performance, waivers, and risk mitigation
The independent review panel found no impediment to the shipment of J1 VIIRS
STAR SDR and EDR teams contributed greatly to the waiver studies prior to the PSR, and will continue to develop mitigation for the waivers
J1 VIIRS relative spectral response functions (RSR) is made available by the SDR team
Birthday cake celebrating the JPSS J1 VIIRS shipping on February 2015

## Slide 44: J1 VIIRS SDR Support
J1 VIIRS Waiver mitigation
  Developing mitigation for JPSS J1 VIIRS DNB nonlinearity at high scan angles (aggregation mode change), in collaboration with NASA flight;
  Aggregation mode options will be fully tested with the Algorithm Development Library (ADL) at STAR before delivery to the operations, together with all other parameters for J1 VIIRS;
  Prelaunch DNB low light testing (with SIS100) is also found useful for improving shortwave infrared channel characterization (such as at 2um, which will benefit ocean color & aerosol applications) ;
  Other changes include saturation handling.
Initial version of the Post-launch Tests (PLT) for VIIRS has been developed;
Currently evaluating and generating the 40+ LUTs required for the IDPS/ADL ground processing system.
J1 VIIRS DNB Aggregation Mode Trade Study
J1 VIIRS SWIR Low Radiance Response from RC2 P4
56.06

## Slide 45: JPSS-1 OMPS SDR Status
Decompression Subroutine
  A new subroutine to decompress Flight Software 6.0 compressed data. Decompression will effectively double our data rate from the instrument to the ground.
Small FOV SDR processing to the OMPS Nadir Profiler and Nadir Mapper
Aggregator Subroutines
  A new subroutine for the Nadir Mapper to aggregate small Field-of-View data into standard FOVs prior to SDR processing.
  A new component of the Nadir Profiler “glueware” to aggregate small SDR FOV measurements into standard FOVs.
Model Based Wavelength Shift is developed
  A branch of the code to compute model estimates of the wavelength shifts.
Filling of Sparse Spectral Counts
  A branch of the wavelength scale adjustment code to interpolate and extrapolate counts for unmeasured rows using the relative solar irradiance values. This allows continued use of the current stray light correction procedure.

## Slide 46: OMPS NM Architecture
RDR
vRDR
SDR
APID Filter
Decompressor
Aggregator
Offline Processing/Archive
SNPP HCS Lo-Res
J‑1 HCS
Hi-Res, Compressed
New Code
Existing Code
Legend:
SNPP HCS
Hi-Res
IDPS SDR Process

## Slide 47: Summary and Conclusions
  Suomi NPP instrument calibration and validation tasks have been completed successfully and all the SDR products have been used in NOAA operations
  NOAA has developed an Integrated CalVal System (ICVS) for long-term monitoring (LTM) of all SNPP/JPSS/GOES-R/METOP instruments
  CrIS, ATMS, VIIRS and OMPS have stable performance with the key instrument parameters (e.g. noise, bias) meeting or exceeding the requirements
  SDR teams developed innovative sciences and algorithms for improving and refining the products processing system, e.g., CrIS full spectral resolution processing and ATMS full radiance processing, VIIRS DNB straylight corrections.
  SDR teams are being participated with the members from NOAA, NASA and universities and government labs. Transitions of new calval sciences from research to operations are going well
  SDR teams start working on J1 prelaunch characterizations of all the instruments, preparing for J1 SDR algorithm upgrades.
  Documentation of all the SNPP SDR sciences and operational codes have been completed, including ATBD and user manuals, error budgets. Peer-review papers have been published in JGR special issue and other high quality journals

## Slide 48: JGR Special Issue on Suomi NPP CalVal
34 papers have been accepted in AGU Journal Geophysical Research Special Issue on Suomi NPP satellite calibration, validation and applications.
Guest Editor: Fuzhong Weng