## Slide 1: Space Weather Products in AWIPS2
Steven Hill, NOAA/SWPC
SWPC: Chris Lauer, Ratina Dodani, Kelvin Fedrick, Mike Carpenter, Ann Newman, Chris Balch, Bob Rutledge, Rob Steenburgh, Brent Gordon
NCO: Shova Gurung, David Plummer, Stephen Gilbert, Jason Travis
NGDC: Johnathan Darnel, Janet Machol, Bill Denig, Pau Loto’aniu, Rob Redmon

## Slide 2: Space Weather Products in AWIPS2
Integrating space weather (including GOES) data into AWIPS2
GOES-R space weather instrumentation and products
Data fusion
Data path from IDP GOES-R product generation to SWPC to AWIPS2
Test operations with GOES 13-15 data

## Slide 3: Not Exactly a Science Issue, but…
GOES Space Weather Data have previously been developed and managed exclusively by SWPC
For GOES-R
  GOES-R program is developing the L1B products
  NGDC is developing the L2+ algorithms and processing system
  NWS IDP will host operational L2+ processing
  AWIPS2 will replace many custom SWPC systems, not just for GOES SWx data, but also for all other SWx data

## Slide 4: AWIPS2 Context
SWPC provides data pipeline
NCO provides AWIPS2 applications
AWIPS2 Functions include:
  Image ingest, rendering, animation and analysis
  Time series data (GOES, ACE, STEREO, DSCOVR)
  Coded messages, events, regions, other text I/O
  Ground magnetometer data
  General forecaster applications (Products, Alerts…)
  Enlil applications: SPI, CMENT, CAT
  Model ingest, rendering and animation

## Slide 5: SWPC Reliance on Satellites
Most Products Require Satellite Data
  95% of SWPC products use satellite data
  Only 10% of products can be produced without satellite data
Two of the Three Space Weather Scales are Derived solely from Satellite Observations
Future Satellite Missions are Critical
  DSCOVR: Continuity of observations from L1
  GOES-R: Continuity of observations from GEO
  COSMIC II: Expanding real-time observations on a global scale
Aurora Location and Intensity Model: Driven by solar wind data measured at the L1 point (1% of the distance between Earth and sun

## Slide 6: GOES R Instruments
EXIS - Ultraviolet and X-ray Irradiance Sensors (EXIS): X-ray sensor, expanded dynamic range and flare location
SUVI – Full-disk extreme ultraviolet imager: Active region characterization, filament eruption, and flare detection
SEISS – Electrons, protons, heavy ions – Surface charging, internal charging, single-event upsets
MAG - Detection of geomagnetic storms and magnetopause crossing, energetic particle products, model validation

## Slide 7: Data Integration and Fusion
Data fusion for forecaster interpretation
  Solar Image overlays for situational awareness
  Over-plots of solar wind measurements vs. models
Notes: Enlil run from 2012-03-14

## Slide 8: Example New/Improved Products
SUVI
  Thematic maps (multispectral pixel classifier) improvements
  Bright regions – associated with solar active regions
  Flare location – Solar eruptions seen as hottest & brightest of bright regions
  Coronal Hole Boundaries – dark areas of strong, outflowing solar wind
SEISS and Magmetometer
  Electron and Proton Densities and Temperatures (Moments)
  Magnetopause crossing

## Slide 9: Demonstration(s)
Proxy data
  GOES 13-15
  ACE
  SDO
Requirements and Specifications
  Latency: < 15 sec for time series; < 1 min for images
  Formats: XML for time series; FITS for images
Reliability
  File type must be easily and quickly validated, self-describing, etc.
  System elements must be robust against interruption and corrupt data
Other Guiding Principles:
  Minimize technical debt
  Minimize maintenance
  Maximize extensibility (easy to add new data sets)

## Slide 10: Solar Imagery on AWIPS2
SDO 19.3nm and HMI magnetogram data
Science level data now accessible to forecasters via FITS format
Quantitative images with accurate navigation

## Slide 11: Time Series data on AWIPS2
ACE and GOES data
Data formats and samples generated
Encoders and decoders written
Prototype pipeline developed
Preparing for operational deployment of the data pipeline

## Slide 12: Conclusion
Substantial progress toward highly reliable system
Integrating a system very unlike prior GOES space weather data systems
Components developed across organizations (GOES-R, NGDC, NCO, NWS, and SWPC)
AWIPS2 image and time series data will soon be available to forecasters in real-time