## Slide 1
GOES-R Product Readiness and Operations Team: Pre-Launch Preparation
Wayne MacKenzie
GOES-R Product Area Lead
NESDIS/OSPO/SPSD
2015 NOAA OCONUS Proving Ground Meeting
Anchorage, AK
May 15, 2015
Notes: Exciting preview of GOES-R-like capabilities. Shown here is the 1km, 1-minute Visible band imagery from GOES-14 when it was in the Super Rapid Scan Schedule. Another great example of how GOES-R will routinely (not just in Super Rapid Scan), be able to provide insight to how the weather IS developing, instead of how the weather WAS developing.
The GOES-R ABI will have sixteen spectral bands vice five (3 times more),
four times the spatial resolution, and
more than five times faster temporal coverage than the current system.
Mode 3 generates 3 times more files than Mode 4.
New Capabilities come with computational cost.
See Talks for GOES-R Data Volumes:
Schmit - ABI
Goodman - GLM
Denig - Space Wx
Metcalf - DCS
Seymour - GRB & HRIT/EMWIN
My Talk is going to focus on what Users should expect to see leading up to and during the Joint Operations of GOES-13/14/15 & GOES-R.

## Slide 2: Slide Collaborators
Jaime Daniels – STAR AWG Lead
Steve Goodman – GOES-R Program Scientist
Bob Iacovazzi – GOES-R L1b Cal Val Lead
Satya Kalluri – GOES-R Development, Integration, & Test
Heather Kilcoyne – GOES-R Product Readiness Deputy & Quality Lead
Maurice McHugh – GOES-R Product Distribution & DOE-4 Lead
Donna McNamara – ESPC Data Access Manager
Tim Meisenhelder – GOES-R DOE Data Lead
Thomas Renkevens – OSPO/SPSD Deputy Division Chief
Tim Schmit – STAR@CIMSS ABI Science Lead
Tom Schott – OSGS Satellite Products Manager
Matthew Seybold – GOES-R Data Operations Manager
Chris Sisko – OSPO/MOD JPSS Data Operations Manager
Nikki Wilcox – GOES-R DOE-0 and DOE-3 Lead
Walter Wolf – STAR Algorithm Integration Team (AIT) Lead
Notes: I work with a great number of tremendously talented people spread across the NOAA organization and I greatly appreciate their collaboration.

## Slide 3: Outline
Role of the PAL
Pre-Launch Activities
  PRO Team
  DOEs
  Cal/Val Activities
    AWG/CWG Participation
Post-Launch
  Current Ops vs GOES-R Obs
  User Support

## Slide 4: GOES-R PAL is Everyone’s PAL
High-level Role:
  Interface between satellite operations, user community and research community.
What does that mean for GOES-R?
  Work with the AWG to ensure correct implementation of the baseline algorithms for GOES-R
  Work to get new products into the GOES-R Ground System
  Pre-Launch: Participate in Ground System Testing
  Pre-Launch: Participate in Cal/Val activities
  Post-Launch: Interface with users during operations to resolve issues/anomalies and answer questions about L2 products

## Slide 5: PRO Overview & Scope
Product Operations Manager
“OSPO DOM”
Matt Seybold (OSPO)
Deputy – Heather Kilcoyne (Program)
Alg & Product Development Lead
Satya Kalluri (OSGS)
Product Quality Lead
Heather Kilcoyne (Program)
Product Operations Lead (includes Cal/Val L2+) “PAL”
Wayne MacKenzie (OSPO)
UPS Operations Lead
(GRB, HRIT/EMWIN) “PAL”
TBD NOAA Fed (OSPO)
User Services
TBD NOAA Fed (OSPO)
Cal/Val L2+ & L1 Support
Elizabeth McMichael
Cal/Val L1
Bob Iacovazzi
L1 Cal Tools
Dave Pogorzala
Dev Support
Randy Race
GOES-R Assets
Change Support
Ryan Williams
Dev I&T
Harris
Non-GOES-R Assets
CWG
Fred Wu (STAR)
AWG
Jaime Daniels (STAR)
GRB Simulators
Harris IT Services
Interfaces with External (Non-GOES-R) Assets
U/S & Cal/Val L2+ Support
Kathryn Miretzky
Vacancies
UPS Support
TBD Contractor

## Slide 6: PRO Team Activities
Product Definition & Users Guide (PUG), metadata, and support POCs
Calibration and Validation Planning and Rehearsals via Data Operations Exercises
Science Products and Tools Verification & Validation
Finalizing Anomaly Tracking, Configuration Management, Integration, Test, and Check-Out Processes
Formalizing Mission Notice Language and SOPs
Reviewing Transition & Handover Steps and Timelines
Setting ‘First Light’ Imagery & Data Release Strategies
Working on SOPs for GOES-R mode changes and mesoscale domain defaults and changes
  Assisting NWS in updating their existing GOES-13/14/15 RSO request SOPs to also handle GOES-R
  Writing SOPs for OSPO/SAB to request GOES-R mode and domain changes
  Writing SOPs for ESPC Help Desk to receive and transmit requests to GOES-R Satellite Operations
Initiating Processes for Baseline Product Enhancements and New Products

## Slide 7: DOE Activities

## Slide 8: Data Operations Exercises (DOEs)
DOEs are mission rehearsals executed by the Data Operations team
DOEs provide incremental readiness to prepare systems, operators, processes, and teams to support mission operations
Conducted in a “rehearse like we fly” manner
Both nominal and anomalous conditions are exercised
  Problems encountered are recorded and opened for investigation
  Unscripted events are injected including failover scenarios
  Some long duration DOEs are planned to satisfy consumers’ needs
Goal is to ultimately exercise the entire ground system by processing various data sets from end-to-end, from L0 through L2+, including PDA in DOE-3 and DOE-4
DOE-4 will include participation by the NWS TOWR-S (Total Operational Weather Readiness - Satellites) project which is incorporating distribution to elements of the AWIPS community
CBU: Consolidated Back-Up in Fairmont, WV
Notes: Photo: CBU: Consolidated Back-Up in Fairmont, WV

## Slide 9
AWG Proxy Team ABI Image Triplet Test Datasets Delivered to the GOES-Program
ABI Image Triplet | 137W | 89.5W | 75W
Model | WRF | WRF | WRF
Number of times | 7 | 7 | 7
Time range | 20:00-20:30UTC | 20:00-20:30UTC | 20:00-20:30UTC
Day | 04-Jun-2005 | 04-Jun-2005 | 04-Jun-2005
Sectors | FD, CONUS, MESO | FD, CONUS, MESO | FD, CONUS, MESO
Types | GRB, VAL | GRB, VAL | GRB, VAL
Navigation | FGF | FGF | FGF

## Slide 10: GOES-R ABI High Fidelity Simulated Datasets
Atmospherically realistic data generated via combination of high spatial resolution numerical model runs and advanced ‘forward’ radiative transfer models
All 16 bands, various coverages (FD, CONUS, Meso), spatial resolutions, and formats (GOES-R Fixed Grid Format, NetCDF)
Used by AWG product teams and in a number of GOES-R Proving Ground demonstrations
Used to support ABI waiver analyses
Planned use in GOES-R Ground System verification testing activities
AWG Proxy Team at CIMSS
Notes: Successive Order of Interaction (SOI) forward radiative transfer model
These high fidelity simulated datasets are important for pre-launch algorithm development, testing, verification, and user readiness activities

## Slide 11: What happens in each DOE?
 | DOE-0 | DOE-1/2 | DOE-3 | DOE-4
Dates | Nov 1-5, 2014 | June 15-30 (16 days) | Aug 20-Sept 8 (20 days) | Oct 5-Nov 11 (37 days)
Input Datasets | Triplet Data | Triplet Data | Triplet Data | Near Real-Time Simulated Data (AAWDS)
PDA Data Delivery to users | No | PDA to select users | PDA to AWIPS ANCF/BNCF, NGDC, CLASS PDA to selected WFOs (CLASS forwards to MSFC) | PDA to NWS/NGDC/CLASS PDA to selected WFOs
Algorithm Change | No | Yes, L2 algorithm change | No | Yes, Cal/INR update test
System Errors | No | System | System | (L1b AAWDS Data)

## Slide 12: DOE Activities
AWG and CWG participating in Ground Segment’s Data Operations Exercises (DOEs)
  DOE-0: NOV 2014: Analysis of DOE 0 data is almost complete
    Input Data: Triplet Dataset (KPPs generated only for L2)
  DOE-1-2: 15-30 JUN 2015
    Algorithm change
    Manually transfer data off of OE to DE (NSOF PPZ DE)
    Input Data: Triplet Dataset (ABI and non-ABI Instruments)
  DOE-3: AUG 2015
    Analyze Space Wx Prototypes and Final Product Set updates (WCDAS DE)
    Input Data: Triplet Dataset (ABI and non-ABI Instruments)
  DOE-4: OCT 2015
    Cal INR update (Fast track LUT process)
    Input Data: near real-time simulated data from CIMSS

## Slide 13
Simulated Cloud & Moisture Imagery (CMI) from the First GOES-R Data Operations Exercise (DOE-0)
DOE-0 Principals:
Dan Linebarger
Mike Andrews
Moji Thompson
Kim Pham
Nikki Wilcox
DOE-0

## Slide 14: CAL/VAL Activities

## Slide 15: GOES-R Product Portfolio Status
Advanced Baseline Imager (ABI)
Aerosol Detection (Including Smoke and Dust) Aerosol Optical Depth (AOD) Clear Sky Masks Cloud and Moisture Imagery (KPP) Cloud Optical Depth Cloud Particle Size Distribution Cloud Top Height Cloud Top Phase Cloud Top Pressure Cloud Top Temperature Derived Motion Winds Derived Stability Indices Downward Shortwave Radiation: Surface Fire/Hot Spot Characterization Hurricane Intensity Estimation Land Surface Temperature (Skin) Legacy Vertical Moisture Profile Legacy Vertical Temperature Profile Radiances Rainfall Rate/QPE Reflected Shortwave Radiation: TOA Sea Surface Temperature (Skin) Snow Cover Total Precipitable Water Volcanic Ash: Detection and Height
Geostationary Lightning Mapper (GLM)
Lightning Detection: Events, Groups & Flashes
Space Environment In-Situ Suite (SEISS)
Energetic Heavy Ions Magnetospheric Electrons & Protons: Low Energy Magnetospheric Electrons: Med & High Energy Magnetospheric Protons: Med & High Energy Solar and Galactic Protons
Magnetometer (MAG)
Geomagnetic Field
Extreme Ultraviolet and X-ray Irradiance Suite (EXIS)
Solar Flux: EUV Solar Flux: X-ray Irradiance
Solar Ultraviolet Imager (SUVI)
Solar Imagery (X-ray): coronal holes, solar flares, coronal mass ejection source regions
Advanced Baseline Imager (ABI)
Absorbed Shortwave Radiation: Surface Aerosol Particle Size Aircraft Icing Threat Cloud Ice Water Path Cloud Layers/Heights Cloud Liquid Water Cloud Type Convective Initiation Currents Currents: Offshore Downward Longwave Radiation: Surface Enhanced “V”/Overshooting Top Detection Flood/Standing Water Ice Cover Low Cloud and Fog Ozone Total Probability of Rainfall Rainfall Potential Sea and Lake Ice: Age Sea and Lake Ice: Concentration Sea and Lake Ice: Motion Snow Depth (Over Plains) SO2 Detection Surface Albedo Surface Emissivity Tropopause Folding Turbulence Prediction Upward Longwave Radiation: Surface Upward Longwave Radiation: TOA Vegetation Fraction: Green Vegetation Index Visibility
Baseline Products
Future Capabilities
GOES-R Key Performance Parameters
Added to Baseline, required for Snow Cover
Prospective Prototype Wrapped Algorithms
Prospective Post-Handover Implementation
2015 NMSC – Convective Initiation
2015 CIMSS - Probability of Severe Wx

## Slide 16: GOES-R Calibration/Validation Program
Goal of the Cal/Val Program is to have Provisional L1b (and CMI) and Beta L2 data products at the Operations Handover to be held about 6 months post-launch
  Provisional = Ready for users to assess in their applications for operational use
  Beta = Product is minimally validated and may contain significant errors
Calibration Working Group (CWG) will conduct Post-Launch Performance Tests to calibrate and validate the L1B data products
  CWG will identify, report and collaborate with instrument vendors to resolve issues with ground segment algorithms
  CWG will modify calibration tables as needed
Algorithm Working Group (AWG) will also perform post-launch analyses to calibrate and validated the L2 data products
  AWG will identify, report, and resolve issues with ground segment algorithms.
  AWG will modify configuration tables as needed.

## Slide 17: Validation and Availability for GOES-R Baseline Products
GOES-R Launch
to 89.5° West
Milestone:
Program Phase:
Pre-Launch | PLT (6 months) | Post-Handover
Operations Handover
(includes Products)
On-Orbit East/West
Operations
Extended Validation
L1b Product Activities
L1b Validation - Products recertified against pre-launch instrument performance
‘First Light’ Data captures shared from Instruments
Insertion of L1b products into GRB service is controlled by ground system and will occur as products are certified
L2+ Product Activities
L2+ Validation – Same certification process as L1b products
However, L2+ certification begins after L1b products and the portfolio will mature at an overall slower rate with some products certified post-Operations Handover
Distribution Testing
Testing of Distribution Requirements for GRB, AWIPS, and PDA will occur with Integration & Test Customers, utilizing a terrestrial test-purpose data flow from Wallops to NSOF
Mission Notifications
Mission notifications will inform users of new product operations and caveats (e.g. GOES maneuver data caveats) leading up to, during, and after Operations Handover
Notes: More precisely: L1b Validation – On-orbit product performance recertified against pre-launch analytically-predicted product performance.

## Slide 18: Leveraging Himawari-8/AHI for GOES-R Readiness
Himawari-8 was successfully launched October 7, 2014 and carries the AHI which is an almost identical instrument to the ABI
Availability of AHI datasets brings an unprecedented opportunity to exercise the Level-2 algorithm developed for GOES-R
NESDIS/STAR is now pulling AHI data from JMA’s Cloud Service
GOES-R Algorithm Working Group (AWG) teams are working to test their product algorithms with AHI data
Special thanks to JMA for sharing data and collaborating with NOAA and NASA during their post launch checkout

## Slide 19
H-8/AHI Winds
HIMAWARI-8 AHI 1/24/2015 2120 UTC
Band 14 (11um) Winds
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
19
Notes: The Himawari-8 Advanced Himawari Imager (AHI) is in the relatively early stages of in-orbit checkout
Over 50,000 AMVS were generated over the FD (~ 4x increase from current GOES)
These winds were generated using 3 FD images separated by 10 minutes. Image registration for these three images was quite good.

## Slide 20: Post Launch Activities

## Slide 21: Current GOES-13/14/15 Capabilities without GOES-R Succession Products
ASOS Cloud Product (clear, broken, scattered, cloudy for 3 layers – high, mid, and low)
Effective Cloud Amount
Evapotranspiration and Drought Map
Tropical Cyclone Formation Probability (TCFP)
Upward Longwave Radiation (TOA and Surface)
Blended products (combination of geo/polar or multi-geo satellites)
  Arctic Composite Satellite Imagery
  Biomass Burning Emissions
  Downward Longwave Radiation (Surface)
  Global Imagery Mosaics (visible, IR)
  Hydrometeorological Products (Rain Rate and TPW)
  Photosynthetically Active Radiation (PAR)
  Rain Rate from land falling tropical cyclones (eTRaP)
  Sea Surface Temperature
  Snow Cover, Ice Cover, Snow Depth, Ice Thickness
NCEP’s product tailoring needs (BUFR formatted files)
Requests for products are prioritized by the NOAA GORWG (Geostationary Operational Requirements Working Group) and submitted to the NESDIS OSAAP & OSGS for consideration
Red highlighted above are within the current JPSS requirements and JPSS is funding.
Blue highlighted are PSDI proposals for GOES-R capability.
Notes: OSAAP is the requirements lead for NESDIS and identify to OSGS what needs to be done and the funding to be used. OSGS will follow the SPSRB process when executing projects. In the future, if a user request comes into the SPSRB it will be sent to OSAAP for validation and determination whether funding is available or not to execute.

## Slide 22: GOES-R Algorithms Used for Development of Non-GOES-R Products
AVHRR
  Cloud Products
  Volcanic Ash Detection and Height
GOES-13/14/15
  ASOS Satellite Cloud Products
  Blended Global Biomass Burning Emissions
  Cloud Products
  Fog and Low Stratus
  Magnetopause Crossings/Location
  Wind Products
CLAVR-x and GSIP processing systems
  GOES-R validation tools used to verify Level 2 Cloud Files
MetOp-B
  Space Weather Products
VIIRS
  Aerosol Optical Depth, Particle Size, and Detection
  Cloud Products
  Cryosphere Products
  Polar Winds

## Slide 23: GOES-R Product Help Team
Dual Capabilities
  GOES-13/14/15
  GOES-R
ESPC Help Desk at NSOF
  Help Ticket submissions
    ESPCoperations@noaa.gov
    (301) 817-3880
  Anomaly Notifications
    Future Subscription Service
  RSO & Meso Requests from SDM
User Services Coordinators at NCWCP: SPSD.UserServices@noaa.gov
  Natalia Donoho (OSPO Enterprise)
  Jason Taylor (OSPO Enterprise)
  TBD (specific to GOES-R)
NESDIS
OSPO (Operations)
NSOF
NCWCP
Notes: This team is specific to GOES-R, the mixed legacy GOES-13/14/15 & GOES-R constellation, and the out-year GOES-S and GOES-T.
U/S Coordinator – Anomaly Reporting, Planned Notifications
Submission of the positions from OSPO to NOAA Human Resources is being conducted in single file serial fashion by priority, so each of the positions is currently in the queue.
EMWIN - direct service that provides users with weather forecasts, warnings, graphics, and other information directly from the National Weather Service (NWS) in near real time
HRIT - provides broadcast of low-resolution GOES satellite imagery data and selected products to remotely located user HRIT Terminals
GRB - provide the primary relay of full resolution, calibrated, near-real-time direct broadcast space relay of Level 1b data from each instrument and Level 2 data from the Geostationary Lightning Mapper (GLM). GRB will replace the GOES VARiable (GVAR) service. The GRB contains the ABI, GLM, space environment, and solar data which drive data flow in the NOAA space and Earth environment research and operational framework

## Slide 24: GOES-R Product Operations Team
Data Operations Manager (DOM) at GSFC/NSOF/NCWCP
  Matthew Seybold
GOES-R PAL (Product Area Lead) at GSFC/NCWCP
  Wayne MacKenzie
  ABI (Advanced Baseline Imager)
  GLM (Geostationary Lightning Mapper)
Direct Readout Services PAL (Product Area Lead) at NSOF
  PALs – TBD & Paul Seymour
  HRIT/EMWIN (High Rate Information Transmission / Emergency Managers Weather Information Network)
  GRB (GOES Rebroadcast)
Legacy GOES-13/14/15 Staff at NSOF/NCWCP
  System Engineers & PALs - Bonnie Morgan, Kay Metcalf, Paul Seymour, Marlin Perkins, Lakel Smith, John Paquette, Derived Product PALs
Data Access including PDA at NSOF
  Donna McNamara (Data Access Manager)
  Chris Sisko (JPSS Data Operations Manager)
Space Weather Products Support at NCEI/CO in Boulder, CO
ABI Products Support for Science Quality at STAR in College Park, MD; Cooperative Institutes
GLM Products Support for Science Quality at STAR with support from NASA MSFC
NESDIS
OSPO (Operations)
NSOF
NCWCP
Notes: This team is specific to GOES-R, the mixed legacy GOES-13/14/15 & GOES-R constellation, and the out-year GOES-S and GOES-T.
U/S Coordinator – Anomaly Reporting, Planned Notifications
Submission of the positions from OSPO to NOAA Human Resources is being conducted in single file serial fashion by priority, so each of the positions is currently in the queue.
EMWIN - direct service that provides users with weather forecasts, warnings, graphics, and other information directly from the National Weather Service (NWS) in near real time
HRIT - provides broadcast of low-resolution GOES satellite imagery data and selected products to remotely located user HRIT Terminals
GRB - provide the primary relay of full resolution, calibrated, near-real-time direct broadcast space relay of Level 1b data from each instrument and Level 2 data from the Geostationary Lightning Mapper (GLM). GRB will replace the GOES VARiable (GVAR) service. The GRB contains the ABI, GLM, space environment, and solar data which drive data flow in the NOAA space and Earth environment research and operational framework