## Slide 1: Readiness of JPSS Data into NWS Operations Brian Gockel NOAA/NWS Office of Observations June 15, 2015 2015 Satellite Proving Ground/User-Readiness Meeting

## Slide 2: Readiness of JPSS Data into NWS Operations
  S-NPP/JPSS Product Flow to AWIPS
  NOAAPort SBN
  S-NPP/JPSS Products Planned for AWIPS
  AWIPS Screen Shots of S-NPP/JPSS Products
Topics
2015 Satellite Proving Ground/User-Readiness Meeting

## Slide 3
S-NPP and JPSS
Space Segment
S-NPP/JPSS
Ground Stations
(Space/Ground Comms Node)
NSOF
CBU
JPSS Ground Segment
NOAA/NWS
AWIPS
NCF
PDA
JPSS
IDPS
NDE/
PDA
JPSS
IDPS
Flow of S-NPP and JPSS Baseline
Products to AWIPS
Alternative, local or secondary data paths not shown.

## Slide 4
Satellite Broadcast Network ~ “NOAAPort”
S-NPP/JPSS Product Distribution
GOES
S-NPP/JPSS
NOAA/NESDIS
NOAA/NWS
DCS
VIIRS Imagery
Soundings etc.
GVAR
NCEP
Hydromet Sensor
Products (e.g., radar, ASOS,
Profiler, River Gages)
TOC
NWSTG
Satellite
Product
Generation
AWIPS
NCF
Guidance &
Model
Products
Satellite imagery
Other Environmental
Satellite Products
SES-1
Satellite
SBN Uplink
Facility (NY)
WFO/RFC/NC Forecasts, Watches Warnings
SBN Users – includes
NWS-internal (AWIPS)
and externals
The SBN disseminates satellite, model, radar and other products to AWIPS and other users
SBN Bandwidth is 60+ Mbps
Only SBN-related product flows shown
SBN
NWS
Networks
SBN Rec.
Antennas

## Slide 5
5
SBN Channels Carrying S-NPP/JPSS Products
Channel Name | S-NPP/JPSS Products | Example Products
NMC/NWSTG |  | S-NPP Point Data (e.g., NUCAPS soundings)
GOES/GINI |  | Legacy GOES Imagery (Mostly CONUS)
GOES-R West |  | GOES-R ABI Imagery (West)
GOES-R East |  | GOES-R ABI Imagery (East)
NMC2/NWSTG2 |  | GRIB2 model/analysis/forecast grids
OCONUS |  | GRIB1 OCONUS Grids, Legacy OCONUS GOES Imagery, DCS
POLARSAT |  | S-NPP/JPSS VIIRS Imagery
EXP |  | Test or Experimental Products

## Slide 6
      VIIRS Imagery Channels for AK Region - added in 2012
          Channel I1 (0.64 um)
          Channel I4 (3.74 um)
          Channel I5 (11.45 um)
      Western Hemisphere NUCAPS (NOAA-Unique CrIS/ATMS Processing System Soundings) – added April 2014
      VIIRS Near-Constant Contrast Imagery – Regional, planned for addition in August 2015
      Blended Products (e.g., Total Precip Water)
S-NPP/JPSS Products Planned for AWIPS SBN Addition

## Slide 7
      Other candidate products, in addition to products on preceding slide, include: VIIRS Channel I3 (1.61um) imagery, S-NPP/JPSS Active Fires Product, Cloud Liquid Water (ATMS – NUP), Snow Products, Sea Ice Characterization and/or Concentration.
      Notes:
      NWS field sites with a polar-satellite direct readout feed and ingest/processing systems receive more expansive product set than that which is available via the SBN.
      All NWS field sites have secondary/local methods for acquiring products that are not on the SBN/NOAAPort.
S-NPP/JPSS Products Planned for AWIPS SBN Addition

## Slide 8
VIIRS Imagery (Channel I4 – 3.74 um)
AWIPS II Screenshots of S-NPP Products

## Slide 9
AWIPS II Screenshot NUCAPS Soundings
Geographical Sectors for NUCAPS Soundings on SBN

## Slide 10
Blending of TPW Product from Multiple Satellites done by NESDIS
AWIPS Screenshot of Blended Total Precipitable Water

## Slide 11
AWIPS II Screenshot of VIIRS NCC Granule
Geographical Sectors for VIIRS NCC
Products on SBN (to be added Aug 2015)

## Slide 12
Backup Slide