## Slide 1: Satellite Products Dissemination Brian Gockel NOAA/NWS Office of Observations June 16, 2015 2015 Satellite Proving Ground/User-Readiness Meeting

## Slide 2: Satellite Products Dissemination
  NWS IDP Ground Readiness Projects
    NOAAPort/SBN Expansion
    NWS GRB/H8 Antenna Project
    NWS Network Projects
      Near-Term CONUS and OCONUS Projects
      Long-Term
    Himawari Full-Resolution Processing and Data Flows
Topics
2015 Satellite Proving Ground/User-Readiness Meeting

## Slide 3
Scope of this Presentation
      The primary emphasis of this presentation is on the dissemination of satellite products into and within NWS.
        In particular, this talk’s emphasis is on network and system upgrades taking place within (or in conjunction with) the NOAA Integrated Dissemination Program’s Ground Readiness Project (IDP/GRP). These projects reside principally within the NWS Dissemination Portfolio.

## Slide 4
4
Satellite Broadcast Network ~ “NOAAPort”
GOES-R, S-NPP, JPSS (and other) Product Distribution
GOES
S-NPP/JPSS
NOAA/NESDIS
NOAA/NWS
DCS
VIIRS Imagery
Soundings etc.
GVAR/GRB
NCEP
Hydromet Sensor
Products (e.g., radar, ASOS,
Profiler, River Gages)
TOC
NWSTG
Satellite
Product
Generation
AWIPS
NCF
Guidance &
Model
Products
Satellite imagery
Other Environmental
Satellite Products
SES-1
Satellite
SBN Uplink
Facility (NY)
WFO/RFC/NC Forecasts, Watches Warnings
SBN Users – includes
NWS-internal (AWIPS)
and externals
The SBN disseminates satellite, model, radar and other products to AWIPS and other users
SBN Bandwidth is 60+ Mbps
Only SBN-related product flows shown
SBN
NWS
Networks
SBN Rec.
Antennas

## Slide 5
5
SBN Channels Carrying Satellite Products
Channel Name | Satellite Products | Example Products
NMC/NWSTG |  | GOES/Polar Soundings and GOES H.D. Winds Radar, GRIB1 Grids, Watches/Warnings
GOES/GINI |  | Legacy GOES Imagery (Mostly CONUS)
GOES-R West |  | GOES-R ABI Imagery (West)
GOES-R East |  | GOES-R ABI Imagery (East)
NMC2/NWSTG2 |  | GRIB2 model/analysis/forecast grids
OCONUS |  | GRIB1 OCONUS Grids, Legacy OCONUS GOES Imagery, DCS
POLARSAT |  | S-NPP/JPSS VIIRS Imagery
AWIPS Data Del. |  | Data not routinely broadcast on other channels
Experimental/Test |  | Test or Experimental Products

## Slide 6
NWS GRB/Himawari Direct-Readout Antenna Project
Planned GOES-R/H8 Antenna Sites |  |  |  | 
NWS Office | East | West | Spare | Himawari
Alaska Region HQ* (Anchorage, AK) |  |  |  | 
Aviation Weather Center* (Kansas City, MO) |  |  |  | 
National Hurricane Center* (Miami, FL) |  |  |  | 
Pacific Region HQ* (Honolulu, HI) |  |  |  | 
Space Weather Prediction Center* (Boulder, CO) |  |  |  | 
Storm Prediction Center* (Norman, OK) |  |  |  | 
NOAA Center for Weather and Climate Prediction (College Park, MD) |  |  |  | 
Weather Forecast Office, Guam (Barrigada, GU) |  |  |  | 
NWS Sites Receiving Passive, Receive-only GOES-R/Himawari Antennas (Some spare antennas not shown).
* Existing GOES Antenna Site
The following sites are scheduled to receive GRB/H8 Re-broadcast antennas:
to be added

## Slide 7
NWS GRB/Himawari Direct-Readout Antenna Project
GWSAS = Geostationary Weather Satellite Antenna System

## Slide 8
NWS GRB/H8 Antenna Project – First Deliveries
SPC
Storm Prediction Center
Norman, OK
NHC
National Hurricane Center
Miami, FL
Melbourne, FL
GRB GWSAS – For College Park, MD
Melbourne, FL – GWSAS Racks

## Slide 9
NWS GRB/H8 Antenna Project – Schedule

## Slide 10
NWS CONUS Network Upgrades Project

## Slide 11
NWS OCONUS Network Upgrades Project

## Slide 12
Long-Term “One NWS Network” Project

## Slide 13
Long-Term “One NWS Network” Project

## Slide 14
Himawari Full-Resolution Processing and Data Flows