## Slide 1: SNPP/JPSS Cal/Val Update NOAA Satellite Proving Ground/User Readiness Meeting June 16th, 2015
Lihang Zhou
NOAA/NESDIS/STAR
JPSS STAR (JSTAR) Program Manager
with contribution from
JSTAR Algorithm and Data Products Algorithm Team Leads/Members

## Slide 2: Users Are Important to JPSS!
JPSS Science ensures scientific expertise, processes and organization structure is in place to meet the level 1 performance requirements.
  Including a well define set of documentation providing artifacts beginning with the traceability of user requirements, to processes for algorithm development/updates, and science performance verification
The science algorithms for the XDRs are well defined and described by algorithm theoretical basis documents (ATBD) and the validation concepts of the XDRs are described in cal/val plans. The verification of performance is carefully reviewed by Program Science and the users.
  SNPP continues to be an excellent risk reduction for JPSS-1, so successful that SNPP is NOAA’s Primary Weather Satellite
Users are continuously engaged and provide feedback to Program Science through support from JPSS Proving Ground and Risk Reduction.

## Slide 3: Suomi NPP and JPSS-1 Instruments
Instrument Type |  | Measurement
 | ATMS - Advanced Technology Microwave Sounder | ATMS and CrIS together provide high vertical resolution temperature and water vapor information needed to maintain and improve forecast skill out to 5 to 7 days in advance for extreme weather events, including hurricanes and severe weather outbreaks
 | CrIS - Cross-track Infrared Sounder | 
 | VIIRS – Visible Infrared Imaging Radiometer Suite | VIIRS provides many critical imagery products including snow/ice cover, clouds, fog, aerosols, fire, smoke plumes, vegetation health, phytoplankton abundance/chlorophyll
 | OMPS - Ozone Mapping and Profiler Suite | Ozone spectrometers for monitoring ozone hole and recovery of stratospheric ozone and for UV index forecasts
 | CERES - Clouds and the Earth’s Radiant Energy System | Scanning radiometer which supports studies of Earth Radiation Budget
3

## Slide 4: JPSS SDR/EDR Products & Priorities
JPSS SDR/EDR Algorithms
Priority 2
KPP
Priority 3
Priority 4
VIIRS SDR
CrIS SDR
ATMS TDR/SDR
VIIRS Sea Ice
Ozone Nadir Profile
Sounding (AVMP, AVTP)
VIIRS Sea Surface Temp
VIIRS Imagery
Ocean Color / Chlorophyll
OMPS SDR
Suspended Matter
VIIRS Cloud (CCL,CEPS,CTH)
VIIRS Cloud Mask
VIIRS Snow (Map, Frac)
Ice Surface Temp
Ozone Total Column
VIIRS Active Fires
Vegetation Indices
VIIRS Surface Type, QST
LST (VIIRS/ATMS)
VIIRS Cloud (CBH, CTP, CTT)
Surface Albedo
Aerosol Particle Size Par.
Aerosol Optical Thickness
Surface Reflectance
Green Vegetation Frac.
Land Surface Emissivity
Polar Winds
AMSR Sea Surface Temp
ATMS Cloud Liquid Water
CrIS Ozone Profile
CrIS OLR
AMSR Precipitation
ATMS Rain-Rate
AMSR Sea Ice
ATMS Sea Ice
AMSR Sea Surf Wind Speed
ATMS Snow Cover/Depth
AMSR Snow Cover/Depth
ATMS Snow-Water Equ.
AMSR Snow-Water Equ.
AMSR Soil Moisture
ATMS TPW
AMSR TPW
Trace Gas (CO, CO2, CH4)
ATMS Moisture Profile
AMSR Surface Type
ATMS Temperature Profile
Veg Health Index Suite
NDE OCC
AMSR TDR/SDR
AMSR Cloud Liquid Water
ATMS Imagery
VIIRS Cloud (COT Day/Ngt)
Color Code:
IDPS Products (Blue)
ESPC Products (Purple)

## Slide 5: Level 1 Requirements

## Slide 6: NUCAPS (CrIS/ATMS Soundings) ATBD

## Slide 7: Cal/Val Process Overview
LTM
Pre_Launch
EOC
ICV
Launch
Beta
Provisional
Validated
Four Phases of Cal/Val:
  Pre-Launch; all time prior to launch – Algorithm verification, sensor testing, and validation preparation
  Early Orbit Check-out (EOC) – System Calibration & Characterization
  Intensive Cal/Val (ICV) – Algorithm Calibration & Validation
  Long-Term Monitoring (LTM); through life of sensors after ICV (Validated) – Sensor Stability & Data Product Quality monitoring
  Algorithm Cal/Val Timeline
We are here for SNPP
We Are Here for JPSS-1

## Slide 8: JPSS Product Maturity
DEFINITIONS | ARTIFACTS (DELIVERABLES)
Beta Product is minimally validated, and may still contain significant identified and unidentified errors. Information/data from validation efforts can be used to make initial qualitative or very limited quantitative assessments regarding product fitness-for-purpose. Documentation of product performance and identified product performance anomalies, including recommended remediation strategies, exists. | Beta Beta PowerPoint Presentation: Performance Evaluation Products Status and Error Matrix Considerations/Know Risks Summary of Findings and Recommendations Readme Document for Data Users (goes to CLASS)
Provisional Product performance has been demonstrated through analysis of a large, but still limited (i.e., not necessarily globally or seasonally representative) number of independent measurements obtained from selected locations, time periods, or field campaign efforts. Product analyses are sufficient for qualitative, and limited quantitative, determination of product fitness-for-purpose. Documentation of product performance, testing involving product fixes, identified product performance anomalies, including recommended remediation strategies, exists. Product is recommended for operational use (user decision) and in scientific publications. | Provisional Provisional PowerPoint Presentation Performance Evaluation Product status and accuracy assessment including error budget Considerations/Know Risks (Closed DRs, and Assessment of any Open DRs) Feedback from key users Summary of Findings and Recommendations Readme Document for Data Users (goes to CLASS) ATBD Users Manuals
Validated Product performance has been demonstrated over a large and wide range of representative conditions (i.e., global, seasonal). Comprehensive documentation of product performance exists that includes all known product anomalies and their recommended remediation strategies for a full range of retrieval conditions and severity level. Product analyses are sufficient for full qualitative and quantitative determination of product fitness-for-purpose. Product is ready for operational use based on documented validation findings and user feedback. Product validation, quality assurance, and algorithm stewardship continue through the lifetime of the instrument. | Validated Validated PowerPoint Presentation Product Evaluation including Quality Flags analysis/validation Product status and accuracy assessment including error budget Identify know issues and assessment (Closed DRs, and Assessment of any Open DRs) Feedback from key users Summary of Findings and Recommendations Readme Document for Data Users (goes to CLASS) ATBD Users Manuals

## Slide 9: JPSS Product Cal Val Maturity Process
JPSS STAR (JSTAR) validates all Sensor and Environmental Data Records and conducts products validation maturity reviews.
Review Panel is comprised of JPSS Program and Project Scientists, key NOAA users (NWS, NOS, NMFS, OAR), external users, Low-earth Orbiting Working Group (LORWG) advisors, product development managers (NDE and IDPS), the algorithm science manager (STAR).
JPSS Program Scientist is the chair of the review panel.
During the review process we assess how well the products are meeting specification and make an overall assessment of each algorithm.

## Slide 11: STAR JPSS Program
STAR JPSS PM
Lihang Zhou
Ocean
Paul DiGiacomo
AIT
Walter Wolf
SDR
Fuzhong Weng
Management Support
Murty Divakarla (Integr)
Xingpin Liu (Quality)
Tess Valenzuela (Budget)
Atmosphere
Lihang Zhou
Lands
Ivan Csiszar
VIIRS
Changyong Cao
CrIS
Yong Han
ATMS
Fuzhong Weng
Aerosol
Istvan Laszlo
Shobha Kondragunta
Soundings
Mark Liu
Tony Reale
Cloud(s) Mask
Andy Heidinger
Imagery
Don Hillger
OMPS
Lawrence E Flynn
Integration Team
Cryosphere
Jeff Key
SfcType
Xiwu Zhan
Ocean Color
Menghua Wang
SST
Alex Ignatov
Ozone
Lawrence E Flynn
EDRs
LST&Albedo
Yunyue Yu
Land – NDVI
Marco Vargas
Active Fires
Ivan Csiszar

## Slide 12: SNPP Maturity Status (Will Include all NESDIS Unique Products for JPSS-1)

## Slide 13: Suomi NPP TDR/SDR Algorithm Maturity
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Sensor | Beta | Provisional | Validated
CrIS | February 10, 2012 | February 6, 2013 | March 18, 2014
ATMS | May 2, 2012 | February 12, 2013 | March 18, 2014
OMPS | March 7, 2012 | March 12, 2013 | April , 2015
VIIRS | May 2, 2012 | March 13, 2013 | April 16, 2014
Impacts of ATMS Data Assimilation on Track Forecast of Hurricane Sandy
ATMS into NCEP operational system: May 25, 2012
Control Run
Control Run +ATMS
Predicted vs. observed track for Hurricane Sandy during October 22 to 29. NCEP 2012 HWRF is revised with a high model top and is initialized with its own background 6 hour forecast for direct satellite radiance assimilation in GSI. Control Run: All conventional data and NOAA/METOP/EOS/COSMIC. It is clearly demonstrated that assimilation of Suomi NPP ATMS radiance data reduces the forecast errors of Hurricane Sandy’s track

## Slide 14: ATMS SDR Reached Validated Maturity (Mar 2014) Note: ATMS Nyquist sampling enables significant noise reduction
ATMS on-orbit performance is significantly better than specification
RSDR – AMSU fov constructed from ATMS oversampled fovs. Averaging ATMS
fovs into AMSU fov reduces original noise by about factor of 3.
Fuzhong Weng, NOAA/NESDIS/STAR ATMS SDR Lead

## Slide 15: ATMS is outperforming AMSU in noise and long-term stability
SNPP ATMS channel 8 - upper tropospheric channel
“equivalent” AMSU channel 7
Impact to NWP degrades over time because noise increases
When ATMS is averaged to AMSU spatial resolution the noise is reduced by a factor of 3

## Slide 16: CrIS SDR Product
S-NPP: radiance spectra in 3 IR bands with the normal spectral resolutions of 0.625, 1.25 and 2.5 cm-1 for the SWIR, MWIR and SWIR bands, respectively
JPSS-1: radiance spectra in 3 IR bands with the full spectral resolution (FSR) of 0.625 cm-1 for all the 3 bands
16
Δσ = 0.625 cm-1
Δσ = 0.625 cm-1
Δσ = 1.25 cm-1
Δσ = 0.625 cm-1
Δσ = 2.5 cm-1
Δσ = 0.625 cm-1
Red lines – full resolution; black lines – normal resolution
Product component: CrIS radiance spectra

## Slide 17: S-NPP CrIS Noise Performance
NEdN computed from Internal Calibration Target (ICT), Deep Space (DS) & Earth Scene (ES)
Specification
ICT NEdN time series
2 Feb 2012
2 Sep 2014
Noise well below specification
Stable instrument performance

## Slide 18: NESDIS Unique CrIS-ATMS Product System (NUCAPS) Products
  Products
  Temperature profile (AVTP)
  Water vapor profile (AVMP)
  CrIS Ozone profile (O3)
  Outgoing Longwave Radiation (OLR)
  Trace Gas (CO, CO2, CH4, SO2, N2O, HNO3)
  File format: NetCDF4
  Cal/Val Maturity Status: Temperature/Water Vapor Profile reached Validated 09/03/2014
  J1 Updates/Improvements:
  Extend NUCAPS for CrIS full spectral data
  Update trace gaseous and OLR products
  Improve surface emissivity
  Enhance microwave retrieval
JSTAR NUCAPS Lead: Mark Liu / NPROVS lead: Tony Reale
SUMMARY ON NUCAPS Retrieval Validation vs JPSS L1RD REQUIREMENTS |  |  |  |  | 
MW+IR TEMPERATURE | RESULTS | JPSS L1RD | MW+IR WATER VAPOR | RESULTS | JPSS L1RD
30 – 300mb | 1.35K | 1.5K | 100 - 600mb | 28.2% | 35%
300mb - SURF | 1.25K | 1.6K | 600mb -SURF | 21.8% | 20%
Notes: RMS Statistics vs ARM TWP, SGP, NSA Dedicated RAOBs

## Slide 19: VIIRS: Next Gen Operational Polar Orbiting Imaging Radiometer
22 spectral bands
  Visible to LWIR
  Spatially registered
Better spatial resolution
  Reduced variation over scan
  Higher resolution imaging bands
High radiometric accuracy
  NIST-traceable
  Supported by on-board calibrators

## Slide 20: VIIRS SDR Reached Validated Maturity (Apr 2014)
 | Requirement (absolute uncertainty for uniform scenes) | Prelaunch and onboard calibration | Validation: Relative to MODIS/CrIS/IASI/other thru Inter-comparisons | Note
VIIRS RSB | 2% typical reflectance; 0.3% stability; 0.1% desirable for Ocean Color Applications | M1-M7: 1.2% M8&M9: 1.5% M10: 1.4% for I1&I2: 1.3% for I3: 1.6% | 2% (±1%) for matching bands | Except bands with very low signal (ex. M11); 0.1% accuracy and stability for OC is very challenging. Geolocation error: expectation is half I-band pixel; achieved better than quarter I-band pixel (1-s)
VIIRS TEB | M12/M13: 0.7%(0.13K)@270K M14: 0.6% (0.26K) @ 270K M15/M16: 0.4%(0.22K/0.24K)@270K I4: 5% (0.97K) @270K I5: 2.5% (1.5K) @270K | Better than 0.13K for all M bands except M13: 0.14K I4: 0.47K I5: 0.23K | 0.1K based on statistical comparison with MODIS and CrIS ER-2/SHIS Aircraft underflight shows excellent agreement M15 0.4 K bias relative to CrIS at 200K (in spec.) | M15 at 190K requirement is 2.1% radiance or 0.56K Geolocation uncertainty: expectation was half I-band pixel; achieved better than quarter I-band pixel (1-s)
VIIRS DNB | LGS: 5% Lmin MGS: 10% Lmin HGS: 30% Lmin | LGS: 3.5% Lmin MGS: 7.8% Lmin HGS: 11% Lmin | LGS: 4% Lmin MGS: 7.7% Lmin HGS: 11.8% Lmin | Geolocation error is a ~10th of a pixel (1-s) on the ellipsoid earth but can exceed 1km (up to 24 km at the edges of scan) without terrain correction

## Slide 21: J1 VIIRS DNB Waiver Mitigation
The STAR VIIRS SDR team has developed mitigation for J1 VIIRS DNB performance waivers since Jan 2015:
Delivered the J1 VIIRS DNB LUT to AIT in early May, 2015. The initial version (v0) of the J1 DNB radiometric calibration LUTs were created based on pre-launch test data;
Two sets of LUTs were generated for J1 DNB, operational option 21 (Op21) and option 21/26 (Op26), and tested with SNPP data;
Vertical artifacts are observed due to mismatch between S-NPP agg mode and OP21 LUT. To remove the artifacts, VIIRS SDR team request to schedule real OP21 data from S-NPP VIIRS;
Geolocation software code is on-track for delivery end of June;
J1 VIIRS DNB Aggregation Mode Trade Study
JSTAR VIIRS SDR Lead Changyong Cao

## Slide 22: VIIRS Imagery EDR
Various VIIRS Imagery examples, depicting details in cloud formations or on the ground which were not seen with other instrumentation.
JSTAR VIIRS Imagery EDR Lead: Don Hillger

## Slide 23: VIIRS Ocean EDRs
  SST Products
  Produced at NDE by the NOAA heritage Advanced Clear-Sky Processor for Oceans (ACSPO) system
  Products are monitored online in near-real time
  iQUAM: in situ SST quality monitor
  http://www.star.nesdis.noaa.gov/sod/sst/iquam
  SQUAM: SST Quality Monitorhttp://www.star.nesdis.noaa.gov/sod/sst/squam
Ocean Color Products:
  Normalized water-leaving radiance (nLw’s) at VIIRS visible bands M1-M5
  Chlorophyll-a (Chl-a) concentration
  Kd(490) (New)
  Kd(PAR) (New)
JSTAR SST Lead: Alex Ignatov
Processor | Mean / Std (Day) | Mean/Std (Night)
IDPS | -0.13 / 0.78 | -0.08 / 0.43
ACSPO | +0.06 / 0.48 | +0.01 / 0.36
NAVO | +0.02 / 0.43 | +0.05 / 0.31
Annual Validation statistics against drifters
(Jun 2013- May 2014)
JPSS Spec: Bias 0.2K; Accuracy: 0.6K
JSTAR SST Lead: Menghua Wang
NOAA JPSS VIIRS Monthly Averaged Chl-a May 2015
http://www.nnvl.noaa.gov/Default.php

## Slide 24: VIIRS Vegetation Index
  Products
  Normalized Difference Vegetation Index (NDVI) from top-of-atmosphere (TOA) reflectances
  Enhanced Vegetation Index (EVI) from top of canopy (TOC) reflectances
  Normalized Difference Vegetation Index (NDVI) from top of canopy (TOC) reflectances (New Product for JPSS-1)
  File format: HDF5
  Cal/Val Maturity Status:
  Validated 04/01/2015 AERB Approved
  J1 Updates/Improvements:
  Addition of a new dataset (TOC NDVI)
  Addition of a new Quality Flag byte (QF4)
  Improved definition of high quality of the product
  Implementation of an EVI alternate (EVI2) algorithm
  Generation of Level 3 products (spatial and temporal composites)
TOA – NDVI February 11, 2015
JSTAR NDVI Lead: Marco Vargas; JSTAR GVF Cal Val Lead: Marco Vargas
  Green Vegetation Fraction products: Declared operational on 02/12/2015

## Slide 25: VIIRS 500m resolution gridded vegetation health provides indication of vegetation stress
NOAA Service Report on the 2014
California Drought included the need to use remote sensing for assessments of temporal changes in the Central Valley configuration, channel shapes, vegetation cover….
June 2012 -2015 Vegetation Health – Note improvement in 2015
due to late spring precipitation which increased vegetation. (temporary reprieve since snow pack is low and dry summer setting up).
Blue areas show irrigation,
If irrigation is cutback,
depending on the magnitude,
VIIRS VH maps in the
central valley can be used
for monitoring
Irrigation areas shown in
upper right map
Notes: Satellite perspectives of california drought

## Slide 28
Cron start
Online Data inquiry
Geo-location & temporal matchup
VIIRS SURFRAD
QC & Cloud Screening
Graphics, Data table, & log
FTP server
Email to users
End
Product validation against in-situ data (AERONET, SURFRAD, BSRN etc.)
Vegetation index
Albedo
LST
SDR impact and sensitivity analysis and feedback
Active fire product anomaly
Surface Type
USGS / NOAA Land Product Characterization System
Products are evaluated by SPSRB for NOAA Operational status.
All Suomi NPP IDPS Land Products achieved Validated science maturity.
High resolution satellite data and in-situ
VIIRS Land Product Maturity and Validation
28

## Slide 29: VIIRS Snow and Ice
  Products &Cal/Val Maturity Status:
  Snow Cover: Binary Map
    Validated 01/08/2014
  Snow Cover: Fractional Snow Cover
    Provisional 12/20/2013
  Ice Surface Temperature
    Validated 01/08/2014
  Sea ice characterization
    Provisional 12/20/2013
  File format: HDF5
  JPSS-1: VIIRS Snow Fraction Algorithm will be improved from the current 2x2 aggregation algorithm (750 m) to pixel by pixel (375 m) algorithm
JSTAR Cryosphere Lead: Jeff Key
New Snow Fraction Product: The new product provides the sub-pixel snow fraction. It is based on the normalized difference snow index (NDSI), also used by NASA for MODIS.
Notes:   Information on ice and snow cover is needed by other EDRs.
  AMSR2 on GCOM-W1 will have other snow and ice products: Ice Characterization, Snow Cover, Snow Depth, and Snow Water Equivalent (SWE). These will be operational later this year (2015) or in 2016.

## Slide 30: VIIRS Clouds
  Products and Cal/Val Maturity Status:
  Cloud Mask: Validated 03/05/2014 Cloud Top (CTH,CTT,CTP), Cloud Optical Depth (daytime), Cloud Effective Particle Size, Cloud Base Height: Validated 09/03/2014
  COD (nighttime), &CCL Provisional 08/20/2014
JSTAR Clouds Lead: Andy Heidinger
NOAA Enterprise Cloud Algorithm: The Cloud from AVHRR Extended (CLAVR-x) is heritage NESDIS operational cloud processing system runs for multiple sensors on different satellites
VIIRS must be combined with CrIS and ATMS to create a multilayered cloud phase
  VIIRS Cloud Top Pressure: Images show VIIRS DB data from UW/CIMSS processed through the NDE Cloud Algorithms in CSPP/CLAVR-x.; Image on the left is a false color image (R=M5, G=M7, B=M15(rev)). March 8, 2015. Orbit 17414.; Cloud Top Pressure (right) is important for Aviation and used in the VIIRS Winds Application.

## Slide 31: VIIRS Aerosol EDR
Products
  Aerosol Optical Depth
  Aerosol Particle Size Parameter (APSP)
  Suspended Matter (SM)
  File format: HDF5 (IDPS), NetCDF4 (NDE)
  Cal/Val Maturity Status:
  AOT, APSP:
    Validated 12/22/2014 AERB Approved
  SM:
    Beta 06/26/2013 AERB Approved
Applications:
  NESDIS satellite-derived air quality products used in Environmental Protection Agency (EPA) Air Quality Index (AQI) forecasts.
  Input to NWS global aerosol models (e.g., biomass burning emissions)
  Suomi NPP VIIRS aerosol products made available in near real time to operational air quality forecasters
JSTAR Aerosol Leads: Shobha Kondragunta and Istvan Laszlo
Fire hotspots
High resolution display of AOD pixels at city road/neighborhood (750 m to 1.2 km) scale
High aerosol concentrations
Low aerosol concentrations

## Slide 32
OMPS Ozone
  Products
  OMPS Nadir Mapper Total Ozone
    Total Column Ozone
    Total Column SO2
    UV Absorbing Aerosol Index
    Effective UV Reflectivity
    NO2
  OMPS Nadir Profiler Ozone Profile
  OMPS Limb Profiler Ozone Profile
File format: HDF5 (IDPS, TC & NP); NetCDF4 (Limb Profile)
  J1 Updates/Improvements
    Higher spatial resolution
Slide courtesy of Larry Flynn
JSTAR OMPS SDR and EDR l Lead: Larry Flynn
SO2 products from processing by K. Yang, NASA OMPS Science Team Member. The data for the low-resolution orbit has 35 cross-track FOVs 50x50 KM^2 at nadir. The high-resolution orbit has 175 cross track FOVs 10x10 KM^2 at nadir. Higher resolution data will be obtained as the baseline starting with OMPS on JPSS01. The data shows the volcanic SO2 plume from Kliuchecevskoi (located at the red triangle) as observed by S-NPP OMPS for October 19-20 2013.
Notes: NOAA has monitored ozone using satellite data for 28 years, with the latest-generation instrument being the Ozone Mapping and Profiler Suite (OMPS) onboard Suomi NPP.
We also compare our satellite estimates of ozone against available measurements in order to improve them.
Ozone Hole figure:
This year’s ozone hole is similar in size to those of recent years as the atmosphere continues to show the effects of elevated chlorine levels from human activity.
The white circle around the South Pole is a region without measurements as scattered sunlight is too weak.

## Slide 33: NOAA Integrated CalVal System (ICVS) Monitor on-orbit performance of NOAA satellite instruments
  Monitors over 400 parameters for 28 instruments onboard NOAA/METOP/SNPP satellites

## Slide 34: Summary and Conclusions
The SNPP Instruments are performing well within specification.
Data are easily accessible via NOAA operations, direct readout, and CLASS.
The scientific maturity of these products are well documented and are easily accessible from the STAR JPSS website and CLASS
Organizational structure is in place, lessons learned from SNPP has been incorporated, and JSTAR teams are ready for JPSS-1, the Cal/Val activities for JPSS-1 are expected to be much accelerated than those for SNPP

## Slide 35: Backup Slides

## Slide 36: Blended Total Precipitable Water (bTPW)
bTPW merges TPW from AMSU, SSMIS, ATMS, AMSR-2, GOES and GPS-Met into a unified resource to provide forecasters no-gap TPW coverage over globe and serves as a very helpful tool for forecasters to identify conditions that could result in heavy precipitation and subsequent flooding, and also compares the blended TPW with the NVAP (NASA Water Vapor Project) weekly mean to generate the global map of Percent of Normal TPW (PCT), which helps forecasters quickly see areas where active weather is occurring and assess the severity of the situation. Near-real-time bTPW products are generated houly , and made available in HDFE-EOS, McIDAS AREA and AWIPS GINI format.
The PNG images and image animation loop tools can be found at http://www.ospo.noaa.gov/bTPW.
Limin Zhao, Ralph Ferraro, NOAA/NESDIS/STAR

## Slide 37: Blended TPW
Percent of Normal TPW - Compares the blended TPW with the NVAP (NASA Water Vapor Project) weekly mean. It helps forecasters quickly see areas where active weather is occurring and assess the severity of the situation. For instance, the “Yellow” areas indicate TPW > 200% of the weekly mean, and are threat areas
Blended TPW – Merges TPW from AMSU, SSMIS, GOES and GPS-Met into a unified resource to provide forecasters no-gap TPW coverage over globe and serves as a very helpful tool for forecasters to identify conditions that could result in heavy precipitation and subsequent flooding.

## Slide 38: Blended TPW
  Current Status
    Operational: since March 2009
    Satellites: N15, N16, N17, N18, N19 and Metop-A/-B, GPS-Met, GOES-E&-W
      Ocean
        MSPPS TPW from NOAA-15, -16, -17, -18, -19 and Metop-A/-B
      Land
        GPS-Met over CONUS, Alaska and Hawaii – primary data source over CONUS
        MIRS AMSU TPW from N18, N19 and Metop-A over CONUS when GPS is not available, and also over other landmasks over global
        GOES over CONUS, and part of east pacific ocean – used to fill the hole when no GPS and MIRS TPW are available
    Products: TPW, Percent of Normal TPW; 16km
    Formats: HDF-EOS, McIDAS area and AWIPS
    Data Access: DDS, ADDE and AWIPS
    The imagery products are also available on the Internet through: http://www.ospo.noaa.gov/Products/bTPW/index.html

## Slide 39: Blended TPW – Animation Tool
  Animation – Near-real time loops of blended TPW and PCT available at: http://www.ospo.noaa.gov/bTPW
  Regions – 15 area of interest regions for zooming in details
  Image Interval – 1 hour, 3, 6, 12 and 24 hours
  Historical Data – up to three months
  Products – Blended TPW and Percent of TPW Normal (PCT)
  Refresh – Hourly with the latest 12 hour data from multi-satellites/sensors
  Map Projection – Mercator
  Coverage – Global Ocean and Land excluding poles (71°N to 71°S )
  Resolution – 16 km at equator
  Format: HDF-EOS, McIDAS and AWIPS
Notes:   Improving analysis and prediction of heavy precipitation and flash flood
  Getting more timely and continuous spatial information about moisture transfer/ “surges”.
  Monitoring of the “atmospheric rivers” (ARs)

## Slide 40: Blended TPW
  The Upcoming Updates
    Update to include S-NPP ATMS TPW: Jul 2015
    Update to include GCOM-W1 AMSR-2 TPW: Sept 2015
    Update to include GPM TPW: Dec 2015
Notes:   Upcoming: S-NPP, Megha-Tropiques, GCOM AMSR-2 to be included in next couple of years
  Beyond, JPSS, GOES-R, GPM, etc.