## Slide 1
Introduction
Land surface temperature (LST) measurement is important for understanding climate change, modeling the hydrological and biogeochemical cycles, and is a prime candidate parameter for Numerical Weather Prediction assimilation models. Development of land surface temperature Environmental Data Record (EDR) for the U.S. Geostationary Operational Environmental Satellite (GOES) R series (GOES-R) satellite mission and the Joint Polar-orbiting Satellite System mission is one of the major tasks of the land product team at Satellite Meteorology and Climatology Division (SMCD), center for SaTellite Applications and Research center (STAR). The LST algorithm for GOES-R mission has been developed based on an emissivity explicit, split window linear regression approach, while the LST product for JPSS S-NPP mission is based on a surface-type dependent, split window regression algorithm. Pre-launch evaluation of the GOES-R LST algorithm using real satellite (proxy) data, as well as simulation data, indicates that it will be a stable and high quality product when high quality surface emissivity data at the thermal infrared band is available. Post-launch monitoring and validation works show that quality of the JPSS S-NPP LST product is equivalent to the NASA MODIS LST product. However, it may be greatly impacted by quality of the VIIRS surface type data. The first validated version of the JPSS S-NPP LST product readiness has been reviewed in December 2014; shall be operationally available March 2015.
Land Surface Temperature Production
for GOES-R and JPSS Missions
Yunyue Yu1, Yuling Liu1,2, Peng Yu 1,2, Jaime Daniels1
1NOAA/NESDIS/STAR, 2Univ. of Maryland
JPSS S-NPP LST Algorithm
Overall, S-NPP/VIIRS LST quality meets the Mission’s requirement, based on the in-situ LST measurements from the U.S. SURFRAD stations during the period from Feb. 2012 to Aug. 2014.
Quality of S-NPP/VIIRS LSTs and MODIS LSTs are similar, based on the comparisons of over 100 VIIRS/MODIS simultaneous nadir observation scenes.
The S-NPP/VIIRS LST production is stable, based on STAR weekly LST monitoring.
Impact of sensor noise is ignorable; impacts of ST misclassification and cloud contamination are significant.
Validated V1 version of the VIIRS LST product will be available March 2015.
GOES-R LST Production
JPSS S-NPP LST Production
A split-window regression algorithm is running for the JPSS/VIIRS land surface temperature, Ts, production:
Ts = a0,i + a1,i T11 + a2,i (T11 – T12) + a3,i (secq – 1) + a4,I (T11-T12)2
where ak, i are algorithm coefficients; i indicates 17 IGBP surface types; q is view zenith angle. T11 and T12 represent the VIIRS sensed brightness temperatures at 11 and 12 micron channels (the split-window).
GOES-R ABI LST Algorithm and Process Chain
Surface type | Day/ Night | datanum | Provisional |  | Beta | 
 |  |  | Bias | STD | Bias | STD
Deciduous Broadleaf Forest | day | 4 | -0.67 | 0.80 | 0.31 | 3.10
 | night | 11 | -0.13 | 1.60 | -0.13 | 1.60
Closed Shrub lands | day | 37 | -0.81 | 1.77 | -1.16 | 1.77
 | night | 57 | -1.37 | 0.80 | -2.48 | 0.63
Open Shrub lands | day | 277 | -0.1 | 1.90 | 0.67 | 1.90
 | night | 327 | -0.88 | 0.79 | -2.38 | 0.79
Woody Savannas | day | 46 | -1.09 | 2.39 | -0.34 | 2.81
 | night | 81 | 1.38 | 1.35 | 1.38 | 1.35
Grasslands | day | 172 | -0.38 | 1.90 | 1.11 | 2.36
 | night | 500 | -0.35 | 1.41 | -0.35 | 1.41
Croplands | day | 266 | 0.14 | 2.95 | 2.39 | 3.54
 | night | 558 | -0.21 | 1.58 | -0.21 | 1.58
Cropland/Natural Veg Mosaics | day | 208 | -0.83 | 1.98 | 0.13 | 2.15
 | night | 459 | 0.47 | 1.94 | 0.47 | 1.94
Snow/ice | day | 97 | -1.16 | 1.67 | -1.95 | 1.70
 | night |  |  |  |  | 
Barren | day | 60 | 0.72 | 1.68 | 0.12 | 2.10
 | night | 87 | -1.17 | 0.88 | -2.67 | 0.88
SURFRAD LST over 6 sites covering the time period from Feb. 2012 to December 2013 |  |  |  |  |  | 
Day
Night
1. Evaluation against SURFRAD Station data
April 19th, 2014
2. Evaluation against MODIS LST data (above: Granule comparison; bottom right: Global comparison)
*The data (2012) is provided by Frank Goettsche, thanks Pierre for sharing the data.
Sample VIIRS LST Maps
Evaluations
A split-window, emissivity-explicit regression algorithm is implemented for the GOES-R/ABI land surface temperature, Ts, production:
Ts = a0 + a1 T11 + a2 (T11 – T12) + a3 e + a4 (T11 – T12) (secq – 1)
where ak are algorithm coefficients, q is view zenith angle; T11 and T12 represent the ABI sensed brightness temperatures at 11 and 12 micron channels (the split-window).
Extract
ABI Inputs
ABI Radiances
ABI Solar-View Geometry
ABI Cloud Mask
Data
Mapping
Cloud
Filtering
Emissivity
Day/Night
Flagging
Land
Check
QC
Control
SW LST
Algorithm
LST
Wrap up
Coeffs LUT
Extract
Ancillary
Data
Dry/Moist
Flagging
Criteria values
ABI Sensor QC flags
ABI Goelocation
NCEP WV
Land/coast Mask
LST
EDR
ABI LST Processing Chain
Other Input
Non-ABI Ancillary Input
ABI Ancillary Input
ABI Sensor Input
ABI Snow/Ice Mask
Evaluations using proxy data
ABI LST Map using SEVIRI data as a proxy (right), and evaluation results using MODIS as proxy (bottom).
Validation sample: Image and histogram plot of LST difference between the proxy GOES-R LST and the MODIS LST. The data is sampled from MODIS Terra, on August 17, 2006.
3. Evaluation against ground station dataset at Gobabeb, Namibia.
Summary
    An explicit split-window algorithm has been applied for the GOES-R ABI LST measurement.
    The algorithm package has been developed and implemented in the mission’s ground system.
    The U.S. SURFRAD station measurement is applied for evaluation of the GOES-R ABI LST data.
    Simulation and proxy satellite data have been used for the pre-launch validation; the requirement is met .
    A validation and monitoring tool is in development.
    The Japanese Himawari-8 satellite data will be used for the pre-launch evaluation.