## Slide 1
Joint Polar Satellite System (JPSS)
www.jpss.noaa.gov
JPSS: The United States next Generation Civilian Polar Orbiting Environmental Satellite System
Harry Cikanek, Director
Joint Polar Satellite System
National Environmental Satellite, Data, and Information Service
U.S. National Oceanic and Atmospheric Administration
U.S. Department of Commerce
9 May 2016
2016 NOAA Satellite Proving Ground/User Readiness Meeting

## Slide 2: JPSS provides…
  …the most critical data for numerical weather prediction
  to enable accurate 3-7 day ahead forecasts, giving high confidence to emergency managers in advance of severe weather events
  …operational weather and environment satellite observations for Alaska and Polar Regions operational forecasting
  …global coverage and unique day and night imaging capabilities in support of broad environmental monitoring and forecasting needs
August 2015 – Washington State Fires
August 2015 - Soudelor
July 2015 Manam Volcanic Eruption in
Papua New Guinea (12 km altitude)
Without JPSS, the U.S. would experience an immediate degradation in weather forecasting capability
Notes: EOP: Executive Office of the President
OSTP: White House’s Office of Science and Technology Policy
JPSS: Joint Polar Satellite System
DWSS: Defense Weather Satellite System

## Slide 3: Top priority is supporting the 5 -7 day forecast SUCCESSFUL!!
ATMS
only
ATMS
& CrIS
Relative Humidity Vertical Slice

## Slide 4
JPSS Applications Advancements
  Sounding Products
  On AWIPS and AWIPS Thin Client
  Demonstrations with operational forecasters at 2015 & 2016 Spring Experiment
  Support storm watches and warnings
  Day Night Band
  NCC/DNB now on AWIPS
  Sea Ice
  Storm tracking at night
  Ground Fog
  Active fires and smoke
  Socio / Economic / Impact assessment

## Slide 5: Feedback from the 2015 HWT Spring Experiment
  All participants answered that they understand the differences between space-based soundings and RAOBs
  Feedback available online
  Articulate Presenter modules are available at: https://www.youtube.com/watch?v=U-w6EBnOzb0
  Blog: http://goesrhwt.blogspot.com/search/label/NUCAPS
  “Tales” webinars: http://hwt.nssl.noaa.gov/ewp/
74%
26%
5%
28%
28%
30%
8%
    Daily Survey Q
    Daily Survey Q

## Slide 6: Blog Post: “NUCAPS Sample” May 13 - Midland, TX
Storms moving east into this environment continued to develop and strengthen
Back west, no new development in environment characterized by weaker instability and less moisture
“I liked it and thought it was useful to have today. My office is in between RAOB sites, so it would be nice to have this additional environmental information.”

## Slide 7: Example Blog Post: “West Texas Soundings” May 19 – Midland, TX
12Z MAF RAOB
00Z MAF RAOB
“The drying of the air at 600-800 mb since 12Z is reflected by intermediate NUCAPS soundings.”
19Z NUCAPS near MAF
“The NUCAPS soundings are a good way to see changes in the airmass since the RAOB soundings have been taken.”
Even if
magnitude is
off, drastic
change and
trend is
significant
& useful!

## Slide 8: New JPSS Snowfall Rate (SFR) Product
Performed very well during 2016 Blizzard – good agreement with radar (MRMS)Product
experimentally available in AWIPS, Sterling WFO discussed the product in its January 23 forecast discussion.
..HEAVY SNOW AND NEAR OR WHITEOUT
CONDITIONS WILL CONTINUE IN THE COMMA HEAD REGION AND DEFORMATION
BAND IN THE AREA BETWEEN INTERSTATES 81 AND 95 AND NORTH OF I-66.
IN THIS AREA...NESDIS MERGED SNOWFALL RATE PRODUCT CURRENTLY SHOWS
SNOWFALL RATES OF 1-2 INCHES PER HOUR. BOTH GFS AND ECMWF SHOW AN
ADDITIONAL FOOT AND HALF OF SNOW THROUGH 06Z SUN BRINGING STORM
TOTALS IN THE 25-30 INCH RANGE IN THAT AREA
Credit: NESDIS/STAR Huan Meng

## Slide 9
Photo taken on April 18, 2016 around Black Horse Golf Club, Cypress TX
VIIRS 30-m flood map around Black Horse Golf Club on April 19, 2016

## Slide 10: Fort McMurray Fire – Alberta Canada 80,000 People Evacuated (entire town)
Credit: CIMSS William Straka

## Slide 11
Mission Status
Clouds and the Earth’s Radiant Energy System
Visible Infrared Imaging Radiometer Suite
Cross-track Infrared Sounder
Advanced Technology Microwave Sounder
Ozone Mapping Profiler Suite
JPSS-1 Spacecraft
  S-NPP
  4 years on orbit - October 28
  Rapid data product transition to operational use
  Primary for weather since 1 MAY 2014
  Excellent health and data availability
  JPSS-1
  Integrated satellite test phase
  On track for early 2017 launch
JPSS-2
  Instrument parts/assembly phase
  Spacecraft kick-off phase

## Slide 12
JPSS-1 Satellite and Launch Site Integration & Test

## Slide 14
JPSS Performance for Users
  Data Products Cal/Val and quality
  Three maturity levels
  Traceability to NIST standards
  Constant quality monitoring
  Transition to enterprise algorithms
  JPSS inherited NOAA legacy and NPOESS heritage
  Developed sustainable / maintainable/compatible suite
User Focused Improvements
  Full spectrum CrIS, direct readout improvements
  Program Science -user readiness/risk reduction to enable quicker/broader utilization
  Half orbit latency, 17km resolution OMPS introduced with JPSS-1

## Slide 15: NOAA Demo Direct Readout Sites to reduce latency for rapid update forecast models and for more timely situational awareness
Currently antennas at Hawaii, Alaska, and Wisconsin, are being used routinely by weather forecast offices using AWIPS’s Local Data Acquisition and Dissemination (LDAD) System

## Slide 16
Summary
  Substantial Progress in 5 years since program started
  Program Base-lined to Focus on Weather mission
  5 instrument suite; S-NPP, JPSS-1, JPSS-2 Missions, Block 2 Ground development
  Passed four years of S-NPP operations, observatory working well, excellent user feedback
  Focus on Users
  Successful rapid user readiness, extensive calibration/ validation, risk reduction
  User involvement in PGRR Initiatives have been critical to operational applications
  Plan for Continuity
  Impact Mitigations identified
  Robust plan in place – ready to be executed
  JPSS-2 sensor acquisitions well underway; JPSS-3/4 sensors to be built at the same time

## Slide 18
Click to edit Master title style
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level
18
Click to edit Master title style
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level
3/23/2015
18
18
Thank you!
For more
information visit
www.jpss.noaa.gov
/NOAANESDIS
/NOAASatellites
@NOAASatellites

## Slide 19: BACK-UP SLIDES

## Slide 20: Two significant product improvements
The full CrIS spectral resolution which will enable carbon monoxide products (SNPP/JPSS-1….)
The improved OMPS spatial resolution providing total ozone at 17 km instead of 50 km, and ozone profiles at 50 km instead of 250 km (J1..)
OMP- Volcano SO2 degassing @ 50 km

## Slide 21
JPSS Applications Advancements
  Volcanic Ash
  Wide swath, near constant resolution
  More detections, better plume monitoring / predictions
  Active Fires
  Fire radiative power
  DNB tracking
  Improved visible resolution/ swath
  Successful field studies

## Slide 22
JPSS Applications Advancements
  Oceanography
  Improved sea surface temperature
  Highly calibrated global ocean color
  Hydrology
  Ice blockage
  Flood prediction / monitoring
  Land
  Green Vegetation Fraction
  Vegetation Stress

## Slide 23: Significant improvement in latency
JPSS
SNPP
Polar region latency improved from 2 hours to 10 minutes
95% of the data is within 50 minutes (taking into account BUFR conversion, etc.)
Between +- 50 degrees latitude ~ 30 minutes
Actual performance will be 50% better than specification

## Slide 24: Recent VIIRS flood product being used by Army Corp of Engineers

## Slide 26
Credit: STAR/MIRS Team